## Slide 1
Technology options and challenges in the design of future ion therapy facilities
Dr. Suzie Sheehy
Senior Lecturer, University of Melbourne
Baker/ANSTO Fellow in Medical Accelerator Physics
@suziesheehy

## Slide 2: Hadron therapy (protons or ions)
First experimental treatment: 1954, Berkeley.
First hospital-based proton treatment facility: 1993, Loma Linda, US.
First treatment facility with carbon ions: 1994, HIMAC, Japan.
Hadron therapy remains a niche in cancer therapy:
22,000 patients/year (2018) treated with particle beams against 25,000,000 patients/year with conventional RT
Protons (and ions) deposit their energy at a given depth inside the tissues, minimising dose to the organs close to the tumour, sparing nearby organs.
Required energy for full-body penetration: 230 MeV protons, 450 MeV/u C-ions.
Slide adapted from M. Vretenar, 10/22/20
Notes: Why?

## Slide 4: Therapy with heavier ions (Carbon and others)
Heavy ions are more effective than protons or X-rays in attacking cancer:
The higher energy deposition (and ionisation) per length generates a large number of double-strand DNA breaks that are not reparable by the cell itself.
The different damage mechanism makes them effective on hypoxic radioresistant tumours
Are more precise, with lower straggling and scattering.
Recent studies show that ion therapy combined with immunotherapy may be successful in treating diffused cancers and metastasis.
So far, 2/3 of cases at the mixed facilities like CNAO are treated with carbon.
The development of ion therapy needs to be supported by tests with other ions (He, O, etc.) and by a strong experimental effort covering: Pre-clinical radiobiology; Medical physics; Animal studies; Clinical trials on patients.
(M. Vretenar)
Slide adapted from M. Vretenar, 10/22/20

## Slide 5: CERN Strategy
Specifications from the scientific community
(Archamps Workshop, June 2018)
Proton therapy is now commercial, 4 companies offer turnkey treatment facilities (3 SC cyclotrons, one conventional synchrotron), and in competition with conventional radiation therapy (X-rays).
Heavy ion therapy (mainly carbon) is still in an early phase (13 facilities worldwide, 4 in Europe) in spite of its several advantages but its diffusion is limited mainly by:
  Size and cost of the accelerator;
  Lack of experimental data.
Opportunity for a strong impact on the medical field with an R&D programme based on critical accelerator technologies for a next generation ion therapy and research facility, smaller, possibly less expensive and more performant than the present reference design.
Accelerator
Lower cost, compared to present (~120 M€);
Higher beam intensities than present (1010 ppp);
Reduced footprint, to about 1’000 m2;
Lower running costs.
Delivery
Fast dose delivery (possibly with 3D feedback);
Equipped with a rotating gantry;
Using multiple ions;
With range calibration and diagnostics online.
Slide adapted from M. Vretenar, 10/22/20

## Slide 6: Future needs/concepts:
Accelerator challenges:
Superconducting magnets (novel CCT/helical coil)
Beamline and beam delivery challenges
Fast extraction and control
High current operation accelerator (synchrotron or FFA?)
Fast switching ion species
Magnetic field interactions
Smaller/cheaper/higher throughput accelerators & gantries
‘FLASH’ proton/ion therapy
  (Higher dose rate/beam current)
Multi-ion therapy:
Dose optimization and conformality using multiple ion species within treatment planning (see M. Safavi-Naeini)
MRI-guided proton/ion therapy
  See P. Keall, B. Oborn et al

## Slide 7: PIMMS was in 2000, new study “NIMMS”
MedAustron, Austria
PIMMS study

## Slide 8: The NIMMS Collaboration
Large number of international partners collaborating with NIMMS (a collaboration MoU is planned):
SEEIIST E. Benedetto, M. Sapinski, S. Damjanovic, P. Grübling
TERA Foundation U. Amaldi, P. Riboni, N. Alharbi
GSI P. Foka
INFN G. Bisoffi, L. Rossi
CIEMAT J. Navarro, C. Oliver, D. Perez
Cockcroft Institute H. Owen
CNAO S. Rossi, M. Pullia
Imperial College K. Long, R. Taylor
MedAustron P. Urschütz
U. Melbourne S. Sheehy, X. Zhang
Interest in joining the collaboration expressed by other partners:
Indian Institutions
Baltic Institutions
CERN contributors, who have in different ways contributed to the study:
M. Vretenar, A. Lombardi, V. Bencini, D. Gibellieri, A. Grudiev, H. Pommerenke, S. Ramberger, M. Khalvati, E. Oponowicz, D. Tommasini, D. Perini, M. Karpinen, etc.
Input from medical community via the ENLIGHT Network (managed by M. Dosanjh with M. Ristova and P. Georgieva)
Input from ion therapy scientific community via M. Durante (GSI) and his International Biophysics Collaboration.
Slide adapted from M. Vretenar, 10/22/20

## Slide 9: NIMMS: three alternative accelerator designs
Linear accelerator
Linear sequence of accelerating cells, high pulse frequency.
Length ~ 53 m
Improved synchrotron (warm)
Equipped with several innovative features: multi-turn injection for higher beam intensity, new injector at higher gradient and energy, multiple extraction schemes, multi-ion.
Circumference ~ 75 m
Improved synchrotron (superconducting)
Equipped with the same innovative features as warm, but additionally 900 superconducting magnets.
Circumference ~ 27 m
Other options considered as less interesting because of cost and/or required R&D: RC synchrotron, FFA, SC cyclotron, PWFA
Slide adapted from M. Vretenar, 10/22/20

## Slide 10: Advanced synchrotron design, key elements
Multiple flat-top operation (from HIMAC, Japan)
Optimisation of multi-turn injection: phase space after 30 turns
(A. Avdic, U. Sarajevo)
Alternative lattice based on Double Bend Achromat cells, with dispersion-free drift sections and only 12 dipoles and 14 quadrupoles (16 dipoles and 24 quadrupoles in PIMMS)
(X. Zhang, U. Melbourne)
Slide adapted from M. Vretenar, 10/22/20
Higher beam intensity for faster treatment (2x1010, 20 times higher)
Multiple energy extraction (multiple flat-tops)
Additional fast extraction for FLASH operation
Redesigned linac at higher frequency, for lower cost and parallel isotope production
Multiple particles: p, He, C, O
Optimised layout of beam transport, for both research and therapy
Design study together with SEEIST project

## Slide 11: The FFA: Fixed Field alternating gradient Accelerator
Advantages:
Rapid variable energy <1kHz
Pencil beam scan quickly in 3D
Protons & carbon for therapy and imaging
Sufficient dose rate, rescanning capability
Design driven by demanding future clinical requirements
Disadvantages:
Similar size to synchrotron
Many novel parts (magnets)

## Slide 12: Alternative tech: Fixed Field Accelerators
This type of accelerator has been built and now studied in detail.
More de-risking needed: scaled down beamline test at UniMelb
S. L. Sheehy et al., Prog. Theor. Exp. Phys. 7, 073G01, July 2016

## Slide 13: Future needs/concepts: work in Melbourne
Accelerator tech/concepts:
Superconducting magnets (novel CCT/helical coil)
Beamline and beam delivery challenges
Fast extraction and control
New synchrotron designs
High current operation accelerator (synchrotron or FFA?)
Fast switching ion species
Magnetic field interactions in beam delivery systems
Smaller/cheaper/higher throughput accelerators & gantries
‘FLASH’ proton/ion therapy
  (Higher dose rate/beam current)
Multi-ion therapy:
Dose optimization and conformality using multiple ion species within treatment planning (see M. Safavi-Naeini)
MRI-guided proton/ion therapy
  See P. Keall, B. Oborn et al
Hannah Norman (joint PhD Manchester): beam dynamics studies with superconducting magnets using pyZGOUBI
Elodie Higgins (Masters): design of a scaled FFA gantry at UniMelb
Jacinta Yap (PDRA): scaled beamline design and future ion therapy design for Australia
Frank Zhang (PhD): novel synchrotron lattice designs for ion therapy and injection/extraction optimisation
Adam Steinberg (joint PhD Manchester): design of an FFA accelerator for ion therapy
Australia should be at the forefront of developing the next generation of ion therapy accelerator, not just becoming a user. We are well underway….

## Slide 14: Future needs/concepts: work in Melbourne
Accelerator tech/concepts:
Superconducting magnets (novel CCT/helical coil)
Beamline and beam delivery challenges
Fast extraction and control
New synchrotron designs
High current operation accelerator (synchrotron or FFA?)
Fast switching ion species
Magnetic field interactions in beam delivery systems
Smaller/cheaper/higher throughput accelerators & gantries
‘FLASH’ proton/ion therapy
  (Higher dose rate/beam current)
Multi-ion therapy:
Dose optimization and conformality using multiple ion species within treatment planning (see M. Safavi-Naeini)
MRI-guided proton/ion therapy
  See P. Keall, B. Oborn et al
Hannah Norman (joint PhD Manchester): beam dynamics studies with superconducting magnets using pyZGOUBI
Elodie Higgins (Masters): design of a scaled FFA gantry at UniMelb
Jacinta Yap (PDRA): scaled beamline design and future ion therapy design for Australia
Frank Zhang (PhD): novel synchrotron lattice designs for ion therapy and injection/extraction optimisation
Adam Steinberg (joint PhD Manchester): design of an FFA accelerator for ion therapy

## Slide 15
Thankyou
Dr. Suzie Sheehy
@suziesheehy
suzie.sheehy@unimelb.edu.au
Please talk to members of my group, many of whom are attending this meeting!