## Slide 1
Beam Profile Monitor at the 1MW Spallation Neutron Source
Shin-ichiro Meigo1), Motoki Ooi1), Kiyomi Ikezaki1), Tomoyuki Kawasaki1), Hidetaka Kinoshita1),
Atsushi Akutsu1), Masaaki Nisikawa1),
Shinpei Fukuta1) and Hiroshi Fujimori2)
1) JAEA/J-PARC, 2) KEK/J-PARC

## Slide 2: Outline
Introduction of JSNS
Beam monitor system at JSNS
  Multi Wire Profile Monitor (MWPM)
  Beam Halo Monitor
Beam flattening system
Development infrared and near-infrared camera system

## Slide 3: Beam transport to MLF
3NBT
3-50BT
3-GeV RCS
50-GeV MR
Neutrino line
Material and Life Science Experimental Hall (MLF)
Neutron target
Muon target
road to coast
Length of BT: 314m
Ep: 3GeV
Power: 1MW
Rep.: 25Hz
JSNS
MUSE
FWHM ~150ns
600ns
600ns

## Slide 4: Targets located at MLF
Muon target
  Carbon graphite (IG430)
  Highest intensity in the world
Neutron target
  Mercury
  Highest pulse intensity in the world
Length 2m
Width 34cm
Mercury target trolley
Proton
Hg
Light Water
Safety shroud
Double wall structure
Thick. 2cm
Diam. 7cm
Rotating target
(6rpm)
Fixed target

## Slide 5
Introduction of JSNS
Beam monitor system at JSNS
  Multi Wire Profile Monitor (MWPM)
  Beam Halo Monitor
Beam flattening system
Development infrared and near infrared camera system

## Slide 6
Beam diagnostics for profile and halo
Monitors at PBW
Imaging Plate(IP)
MWPM
Hot cell
IP
Target
Placed by RH
MWPM
Halo monitor
・SEC
・ TC
Profile monitor and halo monitor (online monitor)
  Multi Wire Profile Monitors (MWPMs) (15 sets located) : SiC wires
  Stationary MWPM at proton beam window (PBW) placed at 1.8 m upstream of the mercury target
2D profile： Residual radiation read by the IP (Offline type)
After beam operation: IP was attached at the target by the remote handling
TC

## Slide 7
Beam profile at mercury target
2-D measurement by IP
Result by MWPM
- Fitting by Gaussian
Width and position for each pulse obtained
Good agreement width result by IP
Profile result by the IP
Fitted by two Gaussian curves
Contribution of primary protons and secondary particles (almost neutrons)
0.1 MW (2009 Dec)
0.2 MW (2010 Dec)
Obtained only 6 days of cooling duration after irradiation of 0.2 MW beam
⇒ Possible for 1MW with
certain cooling time
MWPM at PBW

## Slide 8
Heat distribution at entrance of target station
  Scattering beam at PBW producing heat at target vicinities ( < 1W/cc i.e. 10-4 of peak), which is allowable level.
Beam halo measurements
Hg target
Proton beam entrance at target station
Thermocouples(TC)
PBW Halo monitor TC-type
Vertical (cm)
PBW (Al 5mm-t)
Q=CdK/dt

## Slide 9
Introduction of JSNS
Beam monitor system at JSNS
  Multi Wire Profile Monitor (MWPM)
  Beam Halo Monitor
Beam flattening system
Development infrared and near infrared camera system

## Slide 10: Proton beam at the target
Beam operational status
  Study with 1 MW beam
  User operation with 0.5MW
  Getting narrow storage space
Pitting damage is critical
  Negative pressure attacks
  Proportional to 4th power of the peak current density at target
    Useless beam rastering to mitigate
JSNS harder condition than SNS
  SNS: 60 Hz, Storage ring w/o muon target
  JSNS: 25 Hz, RCS with muon target
Although helium bubbling mitigates the pitting damage, peak reduction is essential.
Pin holes at target of SNS
Target vessel
Here
Damage at
JSNS target
5 cm

## Slide 11: Beam flattening system
Beam edge folding by non-linear optics (octupole magnet)
Octupole magnet: 800 T/m3
Non-linear
Linear
Phase space
Real space (Horizontal)
Position
Divergence
Position
OCT1
OCT2
1m
Horizontal plan
Intensity

## Slide 12: Calibration of MWPM
By narrow beam scanning, sensitivity of wire was calibrated
  Maximum correction ~6%
w/o cor.
w/ cor.
Profile w/o correction
Profile w/ correction

## Slide 13: Beam tuning tool with SAD code
Initial condition
OCT tuning
Fit by observed width and extrapolate to NTG
Extrapolate
MTG
PBW
Fitting region
Acuracy of RMS emittance ~5 %
T=M-1S

## Slide 14
Obtained beam profile
OCT 0A
OCT 698A
OCT 698A
w/ muon target
Flat beam was obtained and lower intensity of beam halo was observed
Good agreement of calculation shown even for w/ muon target
Peak smaller by 14 % and 20 % at horizontal and vertical. Overall 40 % reduced.

## Slide 15: Beam profile at neutron target (calculation)
Ideal shape however slight beam loss detected around octupole magnets which can be reduced by changing duct shape at Q mag
Need develop profile monitor at the target
OCT 0A
OCT 400A
OCT 698A
OCT 1200A
OCT 698A w/ muon target

## Slide 16
Introduction
Beam monitor system at JSNS
  Multi Wire Profile Monitor (MWPM)
  Beam Halo Monitor
Beam flattening system
Development infrared and near infrared camera system

## Slide 17: Development 2D profile monitor
Desirable 2D profile monitor at the target with long lifetime
Unknown lifetime of MWPM
Lifetime of proton beam window (PBW) ~2 years is determined by embrittlement due to helium gas production at the PBW
Gas production rate will be carried out by using dump line and thin aluminum foil with Q-mass spectrometer
Result at SINQ/PSI for 0.6GeV
Y. Dai, et al, J. Nucl Mat. 343 184 (2005)
60cm
VAC
He
PBW
Spent PBW

## Slide 18: 2D profile monitor by thermal
  Low temp(<100C)
For observation of spallation neutron target Infrared with capillary tubes
  High temp(~1000C) :
For observation of rotating carbon target
Near-infrared with fiber scope
(Based on rad hard fiber to up 2 MGy)
PBW
Fujikura Fiber
0 MGy 1 MGy 2 MGy
Mercury target
Camera

## Slide 19: Infrared(IR) monitor
50 °C
150 °C
300 °C
IR Camera
Bundled hollow core fibers of quartz capillary tube coated by polyimide
1m
Heater
Present system can be utilized as monitor for target-temp.
IR camera
Mirror

## Slide 20: Near-IR system
Rad hard fiber scope (Fujikura FIGR-20, 20000 pixels) coupled with near-IR filter
Profile at muon target with high temp can be observed.
Utilize for temp anomaly detection of the target
650 °C
1300 °C
980 °C

## Slide 21: Visible light fiber scope system
SNS monitor (SNS web page)
Observation by luminescence with painting on target vessel is already established at SNS.
Setup for visible light

## Slide 22
New facility at J-PARC for ADS development
TEF-T: For Pb-Bi target test facility
    H-, 25Hz, 400 MeV, 250 kW beam
  High current density (20 mA/cm2) required
    JSNS: 6 mA/cm2
Also long lifetime profile monitor required
250kW

## Slide 23: Summary
Using present beam monitor system, high power beam operation can be performed with highly confident.
To mitigate pitting damage, beam flattening system has been developed. Peak intensity will be reduced by ~30 % intensity of linear optics.
New profile monitor system developing by using fiber system
Acknowledgement:
This work is partly supported by the MEXT Grant-in-Aid for Scientific Research (C) Grant no. 26390114.

## Slide 24: Thank you for your attention
Died on 2nd Sep 2015
R. I. P.