## Slide 1: Summary of the 2014 Beam-Halo Monitoring Workshop SLAC, 19 September 2014
IBIC 2015, Melbourne
2015 September 17
Alan Fisher
SLAC National Accelerator Laboratory

## Slide 2: Workshop Background
  One-day workshop at SLAC following IBIC 2014 in nearby Monterey.
    39 registrants
    11 talks
      All slides are posted on-line at the workshop site at SLAC
  Organizers:
    Alan Fisher, SLAC
    Rhodri Jones, CERN
    Hermann Schmickler, CERN
  Motivations
    Avoiding damage from beam halo in machines such as:
      The LHC high-luminosity upgrade at CERN
      LCLS-2 at SLAC (1-MHz beam with CW superconducting RF)
  Objectives
    Measure a halo density ≤ 106 below density of the bunch core
    Observe halo reduction as collimation is changed

## Slide 3: Topics
  The program was divided into three sessions:
    Invasive techniques
    Non-invasive, non-optical techniques with gas or electrons
    Optical techniques
  Halo measurements were considered in:
    Electron linacs (x-ray FELs)
    Electron storage rings
    Proton storage rings (LHC)
  I will show highlights from all the presentations.
    Original slides where possible
    Some compression and reformatting to fit into today’s schedule

## Slide 4: Workshop Program

## Slide 5
Deutsches Elektronen Synchrotron DESY
Halo Monitoring = Very High Dynamic Beam Profile Measurements; Transversal (and Longitudinal)
  Kay Wittenburg, DESY, MDI
  Kay.Wittenburg@desy.de
Many slides from:
Beam halo and bunch purity monitoring, CAS 2008
Overview of Recent Halo Diagnosis and Non-Destrucive Beam Profile Monitoring, HB2006
see what’s new…

## Slide 6
Sources of halo are:
  space charge forces of the beam
  Mismatch of beam with accel. optics
  beam beam forces
  instabilities and resonances
  RF noise
  Scattering (inside beam, residual gas, macroparticles, photons, obstacles (stripping foil, screens etc.)
  nonlinear forces, e.g. aberrations and nonlinearities of focusing elements
  Misalignments of accel. components
  electron clouds
  Beam energy tails from uncaptured particles
  Transverse-longitudinal coupling in the RF field
  etc.
What is Halo?
DEVELOPMENT OF THE BEAM HALO MONITOR IN THE J-PARC 3-GeV RCS
M. Yoshimoto, IPAC12
Kay Wittenburg

## Slide 7
Towards wire scanner measurements with
Large Dynamic Range (> 106)
Pavel Evtushenko,
Jefferson Lab

## Slide 8: Tail Formation and Phase Space
  Beam dyanmics easily forms tails:
    Parmela simulations of the JLab FEL photoinjector show a tail of 310−3 forming around the core
  The core and tail occupy different volumes in phase space
    Tail measurements vary with position along a beamline, even in a drift:
Pavel Evtushenko

## Slide 9: Wire Scanners with Large Dynamic Range
  Beams with high repetition rates can use pulse counting (CEBAF)
    Coincidence detection helps to reduce background
      Longer counting time (~15 minutes)
  At lower rates use a gated integrator
    Use PMT with low dark current
      A few nA
    Increase the dyamic range using two integrators with input current signals differing by 100
  Logarithmic current-to-voltage converters being evaluated
    Dynamic range of 108 to 1010
Pavel Evtushenko

## Slide 10: Cherekov Converter
  Cherenkov radiator converts shower to visible photons
  Rejects loss from other directions
  Reflective optics focus light into a quartz fiber
  Fiber goes to a PMT outside the tunnel
    Lower background
Cylindrical
reflector #1
Cone
reflector #2
90˚ off axis
parabolic
reflector #2
Optical fiber input
Cherenkov radiator
Pavel Evtushenko

## Slide 11
Two-dimensional and wide dynamic range profile monitor using OTR/fluorescence screens for diagnosing beam halo of intense proton beam
Y. Hashimoto, T. Toyama,
T. Mitsuhashi and M. Tejima
KEK

## Slide 12
OTR screen for beam core observation!
Beam halo
Beam core
Beam halo observation by screen with hole
Toshiyuki Mitsuhashi

## Slide 13
OTR screen for beam core observation!
Beam halo
Beam core
Beam halo observation by screen with hole
Toshiyuki Mitsuhashi

## Slide 14
Fluorescence screen for observation of beam halo in outside
Beam halo observation by screen with hole
Beam core
Toshiyuki Mitsuhashi

## Slide 15
Target assembly
Toshiyuki Mitsuhashi

## Slide 16
Toshiyuki Mitsuhashi

## Slide 17
Alumina fluorescence screen
+OTR screen
Offner relay optical system
Diffuser screen
Image intensifier+ CID camera
Toshiyuki Mitsuhashi

## Slide 18
Superimposed image of beam core (OTR), one image of beam halo nearby core (OTR) and
Beam halo far from core (fluorescence)
Toshiyuki Mitsuhashi

## Slide 19
Difference of order of 10-4 to 10-5
Collimator off
Collimator on
Toshiyuki Mitsuhashi

## Slide 20
Collimator OFF
Collimator ON
Horizontal collimator
Toshiyuki Mitsuhashi

## Slide 21: Using Volume Reflection in Crystals to Collimate and Measure Beam tails
U. Wienands, SLAC
for the T-513 Collaboration

## Slide 22
Uli Wienands

## Slide 23
Uli Wienands

## Slide 24
Uli Wienands

## Slide 25: Ultra-thin Gas Jet for Non-Invasive Beam Halo Measurement
Adam Jeff
CERN & University of Liverpool
Workshop on Beam Halo Monitoring
19th September 2014

## Slide 26
adam.jeff@cern.ch Principle of the gas jet monitor 2 / 17
Generate thin atom gas curtain,
Ionize atoms with primary particle beam,
Extract ions via electric field,
Monitor on MCP, P screen.
Y. Hashimoto et al., Proc. Part. Acc. Conf., Chicago (2001)
Adam Jeff

## Slide 27
e-
Residual Gas Ions
Gas Jet
adam.jeff@cern.ch Test Setup @ Cockcroft Institute 6 / 17
E
Gas Jet Ions
Adam Jeff

## Slide 28
adam.jeff@cern.ch Gas Jet Scanner 11 / 17
Alternative Solution: Gas Jet Scanner
  Generate a thin pencil jet and scan it through the beam
  Like a wire scanner but non-interceptive
  Still collect ions but position not important: not affected by space charge
  Slow scan through halo region, fast through main beam
  Need a way to generate a thin jet…
Adam Jeff

## Slide 29
adam.jeff@cern.ch Matter-Wave Focusing 12 / 17
T. Reisinger, S. Eder, M.M. Greve, H.I. Smith, B. Holst, “Free-standing silicon nitride zoneplates for neutral-helium microscopy”, Microelectronic Engineering 87 (2010)
Matter-Wave Focusing for a Thin Neutral Jet
Smallest zone 100 nm
FWHM at focus 2μm !
Adam Jeff

## Slide 30
adam.jeff@cern.ch Photon Sieves 14 / 17
Photon Sieve replaces clear zones of an FZP with a series of holes
Apodised Photon Sieve reduces higher order diffraction, increases central maximum
+ Sharper focusing
- Lower transmission
+ Easier to manufacture
L. Kipp et al, “Sharper images by focusing soft X-rays with photon sieves”, Nature 414 (2001)
Adam Jeff
Notes: In reality many more rings

## Slide 31
adam.jeff@cern.ch The Atomic Sieve 16 / 17
The Atomic Sieve
Adam Jeff
Notes: Largest holes diameter 1.5 micron
Smallest 80 nm

## Slide 32: Beam profile measurements based on modern vertex detectors and beam-gas interactions
Slides from:
Colin Barschel - TIPP 2014 third international conference on Technology and Instrumentation in Particle Physics
Plamen Hopchev - 9th DITANET Topical Workshop on Non-Invasive Beam Size Measurement for High Brightness Proton and Heavy Ion Accelerators, 16 April 2013
Rhodri Jones (CERN)
SLAC Halo Workshop (IBIC14)

## Slide 33
Rhodri Jones
Vertex Locator (VELO)
Silicon-strip detectors

## Slide 34
Rhodri Jones

## Slide 35: Beam-gas can do more
(LHC fill 3563 2.76 TeV Feb 2013)
Relative measurement of bunch charges
Compared with LHC FBCT instrument
Measurement of unbunched charges (ghost charge faction)
Knowledge of ghost charge is important for the experiments during a luminosity calibration
Rhodri Jones

## Slide 36
Rhodri Jones

## Slide 37: BGV for Halo?
No experience with trying to measure the halo at 4-6 sigmas
Need to deconvolve with tail of vertex resolution
Beam-gas rate will be orders of magnitude smaller at this radial distance
  Currently aim at 100Hz beam-gas per nominal bunch.
  Sampling 0.1% of bunch tail of the bunch  0.1 Hz / bunch
Increasing the interaction rate
Measurement of “average” beam halo possible (2808 bunches)
Increase the pressure (limited by vacuum interlocks)
  factor 10 to 100 may be possible for short times
Combine with gas sheet?
Rhodri Jones

## Slide 38
Scattered electrons as possible probes for beam halo diagnostics
P. Thieberger, C. Chasman, W. Fischer, D. Gassner, X. Gu, M. Minty, A. Pikin
Speculations based on:
The electron backscattering detector (eBSD), a new tool for the precise mutual alignment of the electron and ion beams in electron lenses*
P. Thieberger#, F. Z. Altinbas, C. Carlson, C. Chasman, M. Costanzo, C. Degen, A. Drees, W. Fischer, D. Gassner, X. Gu, K. Hamdi, J. Hock, Y. Luo, A. Marusic, T. Miller, M. Minty, C. Montag, A. Pikin and S. White

## Slide 39: RHIC e-lens with electron back-scattering detector (eBSD)
The beam-beam effect limiting RHIC luminosity will be mitigated with two electron lenses
The 2 m long electron and proton beams propagating in opposite direction in two ~6T solenoids have a width of ~300 m rms.
The misalignment must be < 30 m for the lenses to work properly.
Misaligned can do more harm than good.
BPMs are not quite good enough to guarantee satisfactory alignment.
We will use electrons backscattered by the protons as the “luminosity signal to achieve alignment
The system was recently successfully commissioned with 100 GeV/amu Au and 3He beams
Peter Thieberger

## Slide 40: Electron-gold eBSD “luminosity” scans obtained by steering the electron beam
Date: 4/15/2014
Ion Beam: Gold
Beam energy: 100 GeV/u
Bunch intensity: 7*108
# of bunches: 2
Solenoid Field: 2T
Electron energy: 6 keV
e-beam current: 0.565 A
The electron beam is steered while the ion beam is stationary.
These widths reflect the widths of the electron and the ion beam added in quadrature. The electron beam width is known so the ion beam width can be measured.
Peter Thieberger

## Slide 41
Time-resolved eBSD counts
Ion Beam: Gold
Beam energy: 100 GeV/u
Bunch intensity: 1.1*109
# of bunches: 2
Electron energy: 5 keV
e-beam current: 0.15 A
The background is due to electrons from the residual gas (~5E-10 Torr at pump) .
Electron beam OFF
Electron beam ON
Here the signal to background ratio was ~20 in spite of the low e-beam current and passible misalignment. Several orders of magnitude can be gained as discussed next.
Peter Thieberger

## Slide 42
Possible halo solution
An annular electron collector surrounding the ion beam shouldn’t be difficult to design.
There is no background-producing beam crossing.
The halo detection efficiency can be made azimuthally symmetric
Peter Thieberger

## Slide 43: Optical Techniques: Lyot’s Coronagraph
  We want to image a dim beam halo surrounding a bright bunch
    Compare to viewing the sun’s corona without the benefit of a solar eclipse
      First achieved by Bernard Lyot in 1934
      Mask B blocks the image of the solar disk, but not the corona or the Airy diffraction rings from lens A.
        The sun is about 106 times brighter than the corona. Even these rings are too bright.
      Lens C images plane of A onto aperture D — a “Lyot stop” that cuts the rings
      Lens E images the corona onto photographic film
Bernard Lyot, Monthly Notices of the Royal Astronomical Society 99 (1939) 580

## Slide 44
Coronagraph
for
diagnosing beam halo
T. Mitsuhashi
KEK

## Slide 45
Observation of the sun’s corona by coronagraph
Toshiyuki Mitsuhashi

## Slide 46
Field lens
Lyot’s stop
View from the back side
Toshiyuki Mitsuhashi
Baffles
Objective lens
Mask

## Slide 47
Background sources in coronagraph
Noise from defects on the lens surface (inside) such as scratches and digs.
2. Noise from the optical components (mirrors) in front of the coronagraph.
3. Reflections from inside walls of the coronagraph. Apply baffles
4. Noise from dust in air. Apply dust filter
5. Rayleigh scattering from air molecules.
Not significant in few ten meter optical path
Toshiyuki Mitsuhashi

## Slide 48
Effect 2: Digs on glass surface serve as diffraction sources in the pupil
Toshiyuki Mitsuhashi

## Slide 49
2940
SR beam
electron beam orbit
Half mirror
mirror
source point
coronagraph
Normal imaging system
Beam core + halo (superimposed)
Toshiyuki Mitsuhashi

## Slide 50
Beam core + halo (superimposed)
Toshiyuki Mitsuhashi

## Slide 51
Diffraction tail observed without
Lyot’s stop
Entrance pupil is intentionally rotated by 30º to recognize diffraction tail easily.
30°
Toshiyuki Mitsuhashi

## Slide 52
Single bunch 65.8mA
Exposure time of CCD: 3 ms
Exposure time of CCD: 100 ms
Intensity here: 2.0510-4 of peak intensity
2.5510-6
Background level: about 610-7
Halo in deep outside
Observation for the more out side
Toshiyuki Mitsuhashi

## Slide 53
Injected Beam Imaging at SPEAR3 with a Digital Optical Mask
J. Corbett, K. Tian, and A. Fisher, SLAC, Menlo Park, CA
H. D. Zhang#, R. Fiorito, and A. Shkvarunets, University of Maryland, College Park, MD

## Slide 54: Halo Imaging with a DMA
Mirror array action
Jeff Corbett

## Slide 55: Application to SPEAR3: Image injected beam in the presence of stored beam
Jeff Corbett

## Slide 56: Experimental Setup and data acquisition
9.6m
M1=0.138
M2=3.55
DMD
M3=1
M = M1*M2*M3 = 0.4
7.14m
f=+2m
f=+125mm
f=+100mm
Aperture &
Cold finger
24°
PiMax
Filter wheel
OSR
Source
Injector
READOUT
Gate
Injected beam
Stored beam
SPEAR3
120
13.68 um
BTS

## Slide 57: PSF measurement of the stored beam
2 ms exposure
Increase the mask changing intensity threshold
ND filter
OD =5 to OD = 0
ND 5
ND 4
ND 3
ND 2
ND 1
ND 0
Mask
18 mm
No Mask
f(xo)=ʃg(x)*h(x-xo)dx
F(k)=G(k)H(k)
Jeff Corbett

## Slide 58: Injected beam with stored beam different beam currents
(a)
(b)
Jeff Corbett
Notes: Mention the mask

## Slide 59
Turn 3
Turn 4
Turn 5
Turn 6
Turn 7
Turn 10
Turn 14
Turn 18
Turn 22
Turn 26
Turn 30
Turn 40 (filamentation)
80
3000
Progressive turns with stored beam
Jeff Corbett

## Slide 60
An Amplitude Apodizer for Large-Dynamic-Range Beam Imaging
Pavel Evtushenko,
Jefferson Lab

## Slide 61: Apodization
Imaging: measured distribution is a 2D convolution of source distribution and Point Spread Function (PSF)
PSF is determined by optical system angular acceptance and by the source angular distribution. (OTR, YAG, synchrotron radiation would have different PSF with identical optical system)
Diffraction imposes rather hard limits to dynamic range of imaging optical system
Fourier optics: in image plane intensity distribution - 2D Fourier transform aperture shape with point source (Point Spread Function)
Then it is easy to see that the uniform pupil function, i.e., the sharp lens edge is the problem (besides the uncertainty principle)
Apodization – modification of the pupil function; First considered Gaussian amplitude apodization
Point Spread Functions
Pupil functions – transparency as a function of optics radius
Pavel Evtushenko

## Slide 62: Half-tone dot apodizer
First two apodizers manufactured using half-tone dot process
average optical density (OD) adjusted via the average dot density
2D binary array of 10 µm pixels with transmission of either 0 or 100 %
“error diffusion” algorithm used to translate required OD to dot density
Power spectrum (spatial frequencies) of a pixelated apodizer is different from an ideal continuously variable one
The claim of the “error diffusion” algorithm is that it adds to an ideal power spectrum only at high spatial frequencies – one of the first things to be tested on a bench
If pixels are small enough, the high spatial frequency “noise” does not affect image
NOTE: the apodizer is placed in the Fourier plane
Pavel Evtushenko

## Slide 63: Image “PSF” central line
Pavel Evtushenko

## Slide 64: High-Contrast Imaging and the Direct Detection of Exoplanets
Sandrine Thomas, Ruslan Belikov, and many collaborators
NASA Ames Research Center
Notes: Image of alpha cen

## Slide 65
861 confirmed planets (677 planetary systems)
2740 planet candidates (from Kepler mission)
Wobble method #1: Radial Velocity
(Wobble method #2: Astrometry)
Direct detection
Sandrine Thomas
Notes: Astrometry: from 10pc away

## Slide 66: Direct Imaging Main Engineering Requirements
Contrast
  ~1010 for Earth-like planets
  ~107 for young hot planets and disks
Inner Working Angle
  The smaller the better!
  Typically 1-3 l/D required on missions
Sandrine Thomas

## Slide 67: High Contrast Imaging
Like searching for a firefly next to a lighthouse in San Francisco from Boston
=> Very faint and small in comparison
Upper Scorpius
  Lafreniere et al 2008
Beta Pictoris b
  Lagrange et al 2010
HR 8799
  Marois et al 2008
Fomalhaut b
  Kalas et al 2008
Sandrine Thomas

## Slide 68: Solutions
Diffraction: Coronagraphs
Aberrations: Active and adaptive optics
  Wavefront sensor : Shack-Hartmann, curvature sensors
  Deformable mirror
  Control software
from
telescope
DM system
Coronagraph
Science
camera
WFS
Starlight rejected
by coronagraph
feedback
Diagram of a direct imaging instrument
feedback
Sandrine Thomas

## Slide 69: Principle of Pupil Apodization-type coronagraphs
Image plane
starlight
Telescope pupil
Resulting image
Sandrine Thomas

## Slide 70: Challenge #2: optical aberrations
Image plane
starlight
Telescope pupil
Resulting image
Sandrine Thomas

## Slide 71: Adaptive Optics System for Turbulence Correction
WFS
Feedback
Imager
DM
Distorted wavefront
Corrected wavefront
Sandrine Thomas

## Slide 72: Image sharpening for slow changing aberrations
WFS
Feedback
Imager
DM
Distorted wavefront
Corrected wavefront
Sandrine Thomas

## Slide 73: Starshade
  An alternative to the mask in a coronagraph is a distant “occulter”
    An artificial “moon” far from the telescope to make an eclipse
    A 32-m-diameter “starshade” in the L2 Sun-Earth Lagrange point, 40,000 km from a space telescope
    Flower-petal shape chosen as a kind of apodizer that minimizes diffraction

## Slide 74: Conclusion
Similar issues are seen by your groups and coronagraphy for astronomy.
Need a translation between astronomy and acclerator physics
Sandrine Thomas

## Slide 75: Developing Optical Methods: Bench and Beamline
  Measurements may be dominated by:
    Diffracted, reflected and scattered light from the core
    Stray light from bends reflected along the inside of the beampipe
  Optical techniques should start on a test bench with “halo” that is controllable in intensity and position
    Multiple sources of controllable bright and dim light (lasers, fibers, LEDs)
    Carefully placed black baffles to reduce stray light
    A complete replica of the optics planned for the beamline
  Then test on the real machine
    Does halo change with collimation? Background gas pressure?

## Slide 76: Thank you
  I thank those who participanted at last year’s Workshop.
  I particularly thank the speakers for their talks and for agreeing to post their slides on the conference web site.
  Thank you all for your attention.

## Slide 77: Layout of LCLS-2 at SLAC
Replace 1st km of 3-km copper linac with a superconducting linac.
  CW RF will allow 1-MHz bunch rate (compared to 120 Hz in LCLS)
  Install new Injector, SCRF linac, and extension in sectors 0-10
  Re-use existing bypass line from Sector 10 to beam switchyard (BSY)
  Re-use existing high power dump in BSY
  Add RF spreader to direct beams to dump, SXR or HXR undulators
  Install new variable gap HXR (replacing LCLS-1) and SXR
  Re-use existing transfer line (LTU) to HXR; modify HXR dump
  Construct new LTU to SXR and new dump line
  Modify existing LCLS x-ray optics and build new SXR x-ray line
BSY

## Slide 78: LCLS-2 Linac Design
K. Baptiste, et al, NIM A 599, 9 (2009)
J. Staples, F. Sannibale, S. Virostek, CBP Tech Note 366, Oct. 2006
Sannibale, et al. MOPRI054(IPAC2014)
Wells, et al. MOPRI056(IPAC2014)
Also considering
Cornell DC Gun
Gulliford, et al.
PRSTAB 16
073401 (2013)

## Slide 79: Halo in LCLS-2
  Beam loss in undulators can change field of permanent magnets.
    To operate for 10 years (same as LCLS), losses must be lowered by 104.
    Better collimation, helped by halo monitoring
  Main source is dark current emitted in the gun and RF cavities
    Dark current from linac will have lower energy than beam
      Overbent in first bend of compressor chicane
        Monitor electrons hitting chamber wall to get loss spectrum
    At some phases dark current may travel and accelerate in reverse direction
    Dark current from RF gun will have the same energy as the beam
      Deflect electrons in empty RF buckets and at wrong phase
      Electrons emitted off-axis may be stopped at collimators
      Build an optical monitor at dog-leg after linac?

## Slide 80: Concepts for Halo Monitoring in the LHC
  Several concepts have been discussed for monitoring proton halo in the high-luminosity upgrade planned for the LHC
    Digital micro-mirror array (DMA)
    CID camera with independent integration time for each pixel
    Raster scan of small aperture in front of PMT, with gain controlled by servo loop
    Coronagraph

## Slide 81: SpectraCAM CID Camera
  If you read a CCD fast enough to avoid saturating the brightest pixels, read noise will dominate the dim pixels.
    Sum of dim-pixel values is not equivalent to a long integration.
  A CID (charge injection device) can check the level of charge integrated in any one pixel, without clearing it.
    Clear bright pixels imaging core of beam frequently
    Integrate halo pixels for long periods
    Incur read noise only once, even for dim pixels
  Thermo Scientific’s SpectraCAM CID camera
    Dynamic range of 107
    2048 by 2048 pixels with non-destructive readout of selectable regions
    Random-access (pixel-selective) integration, and no blooming
    Three-stage thermoelectric cooling for low noise
    Gigabit Ethernet output

## Slide 82: SpectraCAM Measurement of Laser Profile
C.P. Welsch, E. Bravin, B. Burel, T. Lefevre, T. Chapman and M.J. Pilon, Measurement Science and Technology 17 (2006) 2035

## Slide 83: Photomultiplier with a Rastered Mask
  Raster scan a mask with a small hole across an optical image of the beam.
  Measure the transmitted light with a photomultiplier.
  Servo the PMT high voltage to maintain a constant signal.
    PMT gain varies as a power of the voltage over orders of magnitude
  Or just insert attenuation as needed.
Hamamatsu R1828-01

## Slide 84: Comparing CCD, CID, and PMT
C.P. Welsch, E. Bravin, B. Burel, T. Lefevre, T. Chapman and M.J. Pilon, Measurement Science and Technology 17 (2006) 2035