## Slide 1: HTc-SQUID Beam Current Monitor at the RIBF
T. Watanabe*, N. Fukunishi, M. Kase
RIKEN Nishina Center
S. Inamori, K. Kon
TEP Corporation
IBIC 2015
16 September 2015
MCEC MELBORNE
HTc: High Critical Temperature
SQUID: Superconductive Quantum
Interference Device

## Slide 2
Preview
Purpose and Importance
How to measure?
What Can the HTc SQUID Monitor Do?
Improvement of Magnetic Shield
Conclusion

## Slide 3
What do we measure?
The current (position) of the DC beam
What are the advantages of measuring a beam using a SQUID?
(1) Nondestructively, (2) Accurately, (3) In real time
Why do we need a SQUID monitor?
  For high-energy heavy-ion beams,
    If a beam is stopped by a Faraday cup,
    (1) the beam can no longer be used;
    (2) there is a danger of melting and activating of cup;
    (3) it is difficult to completely suppress secondary electrons.
HTc SQUID monitor can address all these problems !
Why
Purpose and Importance of High-Tc SQUID Monitor

## Slide 4
Why SQUID?
  DC Current Transformer => Sensitivity ~1mA
Why High-Tc superconductor?
1/1010 !!
Earth’s magnetic field
10-5
T
Environmental
Noise
10-6
10-10
Heart
Motivation
10-13
Brain
1 nA Beam
@10 cm
10-15
Operation
Temperature
Lq. He ⇒ Lq. N2
4.2 K ⇒ 77.3K
Reduction of running costs
Downsizing System
Superconductor
SQUID
- Why we decided to conduct present work -
SQUID
Estimation using Japanese price
0.1 mA Beam

## Slide 5: Where is the SQUID Monitor?
SQUID Monitor
ECR Ion Source Ar
RRC A01 Ar
IRC H11 (NOW) Ca, Zn, Kr, U

## Slide 6
Purpose and Importance
How to measure

## Slide 7
Irradiation of beam
Shielding current is produced
by Meissner effect
Designed to have a bridge circuit
Current is concentrated in bridge circuit
SQUID can detect F with high S/N ratio
Superconductor: Bi(Pb)2-Sr2-Ca2-Cu3-Ox (Bi2223)
Substrate: 99.9% MgO ceramic
Principle of HTc SQUID monitor
Concentrated

## Slide 8
How to measure
What can the HTc SQUID Monitor Do?

## Slide 9
Measurement for
heavy ion beams (2014)
HTc SQUID monitor installed in the IRC beam line
Beam: 48Ca+20 (45.5 MeV/u)
2014/12/10 19:22

## Slide 10
Measurement for
heavy ion beams (2015)
Programed by LabVIEW
Beam: 78Kr+60 (50.0 MeV/u)
2015/ 6/19

## Slide 11
Beam: 40Ar+15 (63 MeV/u)
Discharge of ECR ion source
Amplitudes of ripples in modulated beam
Close up
0 hour (beam off)
0.7 h
3.8 h
FFT analysis
Measurements and analyses
In real time
Without interrupting beam user’s experiments

## Slide 12
FFT analysis
Beam: 78Kr+60 (50.0 MeV/u)

## Slide 13
What Can the HTc SQUID Monitor Do?
Improvement of Magnetic Shield

## Slide 14: Hybrid magnetic shielding system
External
Magnetic Field
1.0 x 10-5 T
3(4) x 10-10 T
1. HTc current sensor with
Ferromagnetic
shielding materials,
2: frame, 3:cap and 4: band.
Calculated result by Opera-3d

## Slide 15
Active noise canceller system
HTc
SQUID
Monitor
3 axis Magnetic Sensor
Hexahedron
3-axis Helmholtz Coil Cage
Specifications
Field attenuation -40 dB
Max. compensation 6 mT
Bandwidth DC(0)～1,000 Hz
AD/DA converter 16 bit
Magnetic sensor DC : 3 axis Flux gate
Magnetometer
*JEOL Ltd. http://www.jeol.co.jp/en/
Canceller OFF
Canceller ON
Surface of Si [110]

## Slide 16
Measurement for
heavy ion beams
Beam: 78Kr+60 (50.0 MeV/u)

## Slide 17
Conclusion
To measure the DC current of heavy-ion beams non-destructively, we have developed a SQUID monitor for practical use in acceleration operation.
We strongly reinforced the magnetic shielding system.

## Slide 18
Thank you for
your kind attention
Tamaki Watanabe
* This work is supported by JSPS KAKENHI Grant Number 15K04749.