## Slide 1: Status of the Intra-bunch Feedback at J-PARC Main Ring
IBIC2015, Sep 12-17 2015, Melbourne Australia
Takeshi Toyama
KEK / J-PARC
Notes: Thank you Mr. Chairman. Good afternoon, ladies and gentleman.
I will be talking about “Beam diagnostic system of the main ring synchrotron of J-PARC”.

## Slide 2
Keigo Nakamura
Kyoto University
Makoto Tobiyama, Masashi Okada,
Yong Ho Chin, Takashi Obina, Tadashi Koseki
KEK
Yoshihiro Shobuda
JAEA
Collaborators
Notes: Thank you Mr. Chairman. Good afternoon, ladies and gentleman.
I will be talking about “Beam diagnostic system of the main ring synchrotron of J-PARC”.

## Slide 3: Japan Proton Accelerator Research Complex
Tokai, Ibaraki
LINAC
40mA
(50mA)
3 GeV RCS
500 kW
(1MW)
30 GeV MR
350kW
(750kW) ← goal
MLF
Hadron hall
n detector
Kamioka
← operation
← one shot
295 km
Kamioka

## Slide 4: Outline
Introduction
  Upgrade history of the J-PARC MR transverse feedback
Feedback during acceleration
  Timing slip
  Timing matching
  Initial result
Summary and prospect

## Slide 5: J-PARC MR parameters
Circumference 1567.5 m
Injection Energy 3 GeV
Extraction Energy 30 GeV
Revolution at injection 5.384us(185.7kHz) RF 1.67MHz
  at extraction 5.231us(191.2kHz) RF 1.72MHz
Harmonic number 9
Repetition time for fast extraction 2.5 s
At high beam power
Collective motion causes beam losses,
other than non-linear resonances (due to space charge).
Transverse oscillation
without FB

## Slide 6: Two obstacles
(1) Injection error & succeeding collective motion
NB ~ 1.67x1013 ppp
2 bunches
xx ~ -7.5
xy ~ -7.0
Injection from the RCS:
circulating beam is kicked by kicker pulse-tail & reflection

## Slide 7: (2) Instability during acceleration
DCCT output
acc. start
turn
Vertical betatron oscillation amplitude
Instabilities has been observed at the beam
power 230kW, with chromaticity ξy=-0.3 .
We avoid this instabilities by tuning chromaticity
ξy=-3.2 .
Observed bunch motion
Keigo Nakamura, et al., IPAC2014, Dresden, Germany
Notes: To increase intensity, the reduction of beam loss is very important.
One of the souce of loss is beam instabilities.
This shows intensity and betatron oscillation ampltitude observed in J-PARiC.
if instabilities occur, betatron amplitude grows and causes the beam loss. [*]
We avoid it by tuning chromaticity xiy=-0.3 to xiy=-3.2.
But large chromaticity also cause beam loss by resonance.
So, we have to suppress instabilities for small choromaicity by some way.
This is the delta signal during the instabilities.
you can see delta signal have internal bunch motion.
so, we think supresstion of internal motion will lead to reduction of beam loss.
----- 会議メモ (2014/06/14 18:43) -----
内部振動を抑える->ビームロスにつながる
----- 会議メモ (2014/06/16 14:39) -----
every 4 turns ploted

## Slide 8
B x B feedback
Bunch-by-bunch (BxB) feedback
slice ~ 590 ns
Beam bunch
Kick

## Slide 9
Intra-bunch feedback
Intra-bunch feedback
slice ~ 10 nsec
Beam bunch
Kick
FIR filter
in iGp12

## Slide 10: Schematic view
oscilloscope
iGp12
injection timing
RF clock
DC offset
x64
x2
Stripline BPM
Stripline kicker
Power Amp.
100KHz-100MHz
Beam
Hybrid
100KHz-200MHz
clock
revolution
Attenuator
X-
X+
DAC+
ADC+
ADC-
DAC-
revolution clk
50Ω
50Ω
For the horizontal (x) plane
Same as the vertical (y) plane
trig. for timing table
Notes: 装置の図、写真

## Slide 11
iGp12 for y
iGp12 for x
Trigger
for timing table

## Slide 12
Without FB
BxB on
+ intra-B on
Without FB
BxB FB on
+ intra-bunch FB on
Oscillation of one bunch slice
Bunch signal every 5 turns
3 GeV injection flat bottom

## Slide 13
Timing slip
Beam
Acc. RF cavity
Tr. kicker
ΔφB(t) beam transit time
Oscillator
iGp12
RF CNTL
RF AMP
RF AMP
φsyn(t) synchronous phase
ℓ
ℓ'
Observing
the beam and
the RF kick
simultaneously
ℓ"
length:
fRF (t)
BPM
Parameters are changing during acceleration upto 30 GeV

## Slide 14
Example of revolution frequency
frev = 185.7kHz  191.2kHz

## Slide 15
Example of synchronous phase
Subject to change depending on the beam tuning
We need rapid parameter optimization
Synchronous phase

## Slide 16
Sampled by iGp12 ← Compare → signals on the stripline kicker
Stripline kicker = directional coupler
can observe
beam signal
RF power from the feedback system
S –signal of stripline kicker
Sampled signal @iGp12
slice#5
marker
@slice#570
marker
@slice#5
Beam
slice#570
Beam
Acc. RF cavity
Tr. kicker
ΔφB(t) beam transit time
Oscillator
iGp12
RF CNTL
RF AMP
RF AMP
φsyn(t) synchronous phase
ℓ
ℓ'
ℓ"
length:
fRF (t)
BPM

## Slide 17
Unit in iGp12
RF CLK x 64
Unit in oscilloscope (kicker) = time (sec)
Referencing the marker #5, 570
scaling and shift
Finally superpose the beam signal by shifting horizontally
the amount of shift = the delay time that we want
Acceleration

## Slide 18: Timing CNTL by preset table
STATE 1 2 3 4 5 . . . . .
External trigger initiates each "STATE"
STATE specifies the delay, filter gain, phase, # of tap
a function of "iGp12"

## Slide 19: iGp12 parameter settings
Injection flat bottom
Acceleration
Injection flat bottom
Acceleration
This trial
This trial
FIR filter parameters
FIR filter parameters
X
Y

## Slide 20
BEFORE
shot513300
Δｘ
Δｙ
AFTER
shot513301
Stabilized
only by switching on
STATE 2
Δｘ
Δｙ
P1+100ms
P2
20 ms/div
STATE
1
STATE
2
STATE
3
STATE
4
STATE
5
STATE
. . .
2015. 7. 1
2 bunches, ~80kW, ~4.2x1013 p
Acceleration
ξx ~ -5.9
ξy ~ -5.2

## Slide 21
AFTER
shot513301
BEFORE
shot513300
Beam Loss
Beam Loss
Beam Intensity
Beam Intensity

## Slide 22: Summary
Transverse intra-bunch feedback during acceleration period
was successful upto P2 + ~80 ms.
・ Horizontal instability at the beginning of acceleration
was suppressed.
・ Stable parameters (delay, gain, frequency) are obtained
Further parameter optimization for further accel. period
Stability check both with experiments and simulations
Contribute high beam intensity upgrade
Prospect