## Slide 1: MEX1 Crystal Spectrometer
Danny Wong
27/05/2021
1

## Slide 2: Table of Content
Where it came from?
What changes were made?
How it is currently implemented?
Engineering GUI
Caproto
Video of Spectrometer
What's next?

## Slide 3: Crystal Spectrometer
The Crystal Spectrometer is one of the first equipment arrived onsite for MEX.
A proven solution used at ESRF
Each assembly has 4 degrees of freedom
23 axes ( 20 for the spectrometer and 3 for the detector stage)
Powerbricks required: 3
3

## Slide 4: Equipment on-site

## Slide 5: Demonstration on how it works
Notes: The function of the crystal spectrometer is to monochromatise the fluorescent X-rays emitted
from a sample and focus them onto the detector. This is performed by an array of five spherically-bent,
crystallographically perfect crystals (Analyser Crystals) arranged in the Rowland circle geometry that
permits selection of a given wavelength, λ, via Bragg’s law

## Slide 6: What changes were made?
Cams were added to the Omega axis
All axes are using absolute encoders
Complex anti-collision switches wired to the limit switches

## Slide 7: Anti – collision switches

## Slide 8: How it is currently implemented?
VM hosted on the Test Environment
GUI created using qe_designer
IOCs are generated using caproto (pure-python channel access protocol library)
Rowland circle calculation using python to get motor position
Send to powerbrick via CA
Moves the motor
Engineering GUI
Python (Caproto)
Powerbrick
motors

## Slide 9: Engineering GUI

## Slide 10: Caproto

## Slide 11: Video of Spectrometer

## Slide 12: What’s next?
Metrology setup to get spectrometer and detector positioner arm to the Rowland circle
Apply offsets and retest useable ranges
Scientist to get familiar with the GUI
Recreate IOC using DLS
Maybe test on existing beamline

## Slide 13
Questions?