## Slide 1
Characterising the Pelletron at the University of Melbourne
Adam Steinberg
University of Manchester & University of Melbourne
Accelerator Technology Forum 2022
0
adam.steinberg@manchester.ac.uk
0
@afsteinberg
Notes: Thanks for taking a look at the slides! Apologies if there are any mistakes.
Any thoughts, comments, or questions? Feel free to let me know, by email or twitter (see details on the slide).

## Slide 2: Thanks To
Hannah Norman [1,2,3] |  |  | 
Jacinta Yap [3] |  | Roland Szymanski | 
Matteo Volpi [3] |  | Stephen Gregory | 
Scott Williams [3] |  |  | 
 |  | Affiliations: | 
 | [1] | University of Manchester, Manchester, UK | 
 | [2] | Cockcroft Institute, Warrington, UK | 
Rob Appleby [1,2] | [3] | University of Melbourne, Victoria, Australia | 
Suzie Sheehy [3,4] | [4] | Australian Nuclear Science and Technology Organisation (ANSTO), Australia | 
… and everyone else in the group
Notes: The names I mention are just those who explicitly gave feedback on or contributed content in this presentation, the group in general is a fantastic place to work that I would highly recommend to others.

## Slide 3: A Pelletron: Schematically
+
-
Animation courtesy of NEC
Maximum beam energy is low
2
Notes: Separation of charge to accelerate particles, no different to capacitor.
These often form the first stage of larger facilities, or exist on their own: the problem is that they can’t reach high energies (limited to tens of MeV, at best) because the high voltages required will lead to dielectric breakdown.
I should also mention that these accelerators are DC: the current should be pretty much constant, unlike in the RF case where it is (generally) pulsed (eg. ‘bunches’ in the LHC)
Electrostatic accelerators were invented in the 20s/30s, and were perfected around the 70s
This motivates the introduction of RF for accelerators, on the next slide…

## Slide 4: The Pelletron Lab: Motivation
Electrostatic accelerator
Protons up to 3.5MeV
  Other ions may be available
Multiple beamlines (3 currently)
  Rotates between beamlines
8.85m
3
With thanks to Jacinta Yap for this diagram
Notes: Pelletron lab serves many projects, but crucially, they are all coarse (they want the beam for what it can do, but don’t care that much about the beam properties themselves). Their experiments are for ion implantation or detector checking, where a reasonably uniform beam can be shot at a target for a long time – but that’s not our goal.

## Slide 5: The Pelletron Lab: Motivation
4
With thanks to Jacinta Yap for this diagram
Boundary condition: available space
Technology for
Ultra
Rapid
Beam
Operation
Notes: As well as making clear that our beamline will attach to the Pelletron somewhere (in one of those spaces), we should state explicitly that our beamline design is very different to those already there (quite obviously: ours must be bendy, to disperse out the orbits at different energies, whereas all the others are straight in order to get maximum beam to various experiments).
Our needs are different to those of the work with the Pelletron, so we need to do experiments to investigate the machine to check that our plans actually will work.

## Slide 6: Particles in Accelerators
5
…
…
Position
Angle
Notes: Particles in *Most Accelerators
Effectively the same thing is true for beam transfer lines (which are usually periodic too, with repeating cells).

## Slide 7: Particles in Accelerators
5
…
…
Position
Angle
Notes: Particles in *Most Accelerators
Effectively the same thing is true for beam transfer lines (which are usually periodic too, with repeating cells).

## Slide 8: Particles in Accelerators
6
Position
Angle
Notes: Particles in *Most Accelerators
Effectively the same thing is true for beam transfer lines (which are usually periodic too, with repeating cells)

## Slide 9: Measuring the Phase Space
Position
Angle
7
Notes: Make a point: measuring the current is really quite straightforward (just stick in a Faraday cup if you want to know how it varies – add in some calibration if you want to know the absolute value), whereas measuring the phase space is a bit more involved

## Slide 10: Measuring the Phase Space
Position
Angle
7

## Slide 11: Measuring the Phase Space
Position
Angle
7

## Slide 12: Measuring the Phase Space
Position
Angle
Slit-Grid Measurement
7

## Slide 13: What Can we Measure?
8
BPM
FC
(NEC Model 80)
For Current and Profiles

## Slide 14: What Can we Measure?
100 µm
200 µm
9
For Slit-Grid
D-Pace Fibre Scanner
Tantalum Sheets

## Slide 15: What Can we Measure?
1445 mm
10
For Slit-Grid

## Slide 16: Beam Current: Constant?
11
Terminal Ripple:
Voltage fluctuations in Pelletron
Notes: Measured inside the Pelletron itself, after the vertical bend.
It turns out, the large drops in current are correlated with oscillations in the ‘terminal ripple’, i.e. the variation in the accelerating voltage: even though the variation is less than 1% of the signal, this can still be hundreds of volts. As we measure after the bend, this voltage variation leads to energy fluctuations, and the beam is lost around the bend.

## Slide 17: Beam Current: Constant?
Reducing the terminal ripple solves part of the problem
12
Notes: The downwards spikes might come from the pellets, but there’s no easy way to determine this

## Slide 18: BPMs Cause Current Drops
13
Before the 90° bend
After the 90° bend

## Slide 19: BPMs Cause Current Drops
Use a BPM…
Before the 90° bend
After the 90° bend
Downstream of the FC
14
How about the beam profiles?

## Slide 20: Beam Profiles
This tells us about the beam at a single point, but not how it evolves
We need to measure the phase space, which can be transported
15
Notes: All the profile measurements in this (and the following) slides were taken on the RED beamline, using the Beam Position Monitor just before the analysis chamber (the metal cylinder at the end).
Here, I should also point out that this measurement is
A different energy to the other’s we’ll see (3MeV, rather than 2MeV)
Taken at a completely different time to the others (so the profiles aren’t consistent)
Several metres downstream of the fibre scanner (which suggests the beam divergence is quite small)

## Slide 21: Phase Space Measurement: Results
Parameter | Value
Beta [m] | 13.000
Alpha | -8.156
ε [mm mrad] | 0.0979
From Covariance Matrix
2MeV protons, horizontal plane
16
Notes: The outlines are (1,2,3)*emittance for a Gaussian fit.
This is the unnormalised emittance (i.e. not *beta*gamma)

## Slide 22: Phase Space Measurement: Results
Repeat measurements vary
Parameter | Measurement |  | 
 | 1 | 2 | 3
Beta [m] | 13.0 | 10.8 | 15.0
Alpha | -8.16 | -7.04 | -9.66
ε [mm mrad] | 0.098 | 0.086 | 0.110
1
2
3
17
Distributions look similar?

## Slide 23: Collaboration is Key
You Might Have
A 5U Pelletron from 1974
A couple of BPMS
YAG Screens & cameras
A few Faraday Cups
We Have
More / better BPMs
Better terminal stabilisation
Misc spare equipment
Energy measurement method
Expertise in control systems
The UniMelb Pelletron has lots of life left in it, and we are keen to collaborate with you
18
Notes: TPS stands for ‘terminal potential stabiliser’

## Slide 24: In Summary
0
adam.steinberg@manchester.ac.uk
0
@afsteinberg
The UniMelb Pelletron is used for many experiments, but has previously not been well characterised
Measurements suggest variation in beam current and distribution, although some may be mitigated
We are keen to collaborate with you on future measurements, and comments or feedback are appreciated
19

## Slide 25: Additional Slides

## Slide 26: Courant-Snyder Parameters (Roughly)
Position
Angle
Beta (range of )
Alpha (- correlation)
ε (phase-space area)
Notes: Particles in *Most Accelerators
Effectively the same thing is true for beam transfer lines (which are usually periodic too, with repeating cells).

## Slide 27: Terminal Ripple is Problem
What is the impact of the terminal voltage on the beam current?
When the terminal ripple is large, the current falls
The frequency and general behaviour of the current can be predicted from the terminal ripple
Note: the actual ripple is probably sinusoidal, but the signal is limited by the gain of the amplifier circuit
When the signal from the dome does something funny (the machine burps), the beam current burps too

## Slide 28: Power Density of the Raw Current Signal
Current
Terminal Ripple
BPM (and harmonics)
Terminal ripple rail-to-rail

## Slide 29: Measurement from FC2 - Drift
How does the current drift over time, without doing anything?
When no adjustments are made, the current varies significantly.
This is usually fixed (manually) by varying the voltage on the steerer close to the ion source.
QUESTION:
What is the source of this long-term drift, and can we correct for it automatically?
The current dropped suddenly so the oscilloscope stopped triggering until I changed the settings

## Slide 30: The Maths of the Slit-Grid