## Slide 1
Research Advances in Key Technologies of Ultra-Large Cryo-plants at TIPC of CAS
Prof. Liqiang Liu Technical Institute of Physics and Chemistry, CAS
April 2023, Melbourne

## Slide 2
Contents
1. Background
2. Advances in Key Parts/Tech.
3. Advances in Systems
4. Conclusions & Prospects
Contents

## Slide 3
1. Background：Scale & Type of Cryo-plant (CP)
Qeq: Equivalent cooling capacity @ 4.5K
S-CL
（QeqW）
M-CP
（Qeq>100W）
L-CP（Qeq>1kW）
UL-CP（Qeq>10kW）
Ultra-Large 2K Cryo Refrigerator
Ultra-Large Hydrogen Liquefier
Ultra-Large Helium Liquefier
Typical Type
Scale Classification

## Slide 4
1. Background：Development journey of CP at TIPC
2kW@20K
Helium CR
Start to develop Helium CP System
250W@4.5K
Helium CR
200W@4.5K
Helium CR
1976
2009
2012
2014
2015
2016
2017
2018
2020
2021
40L/h Helium Liquefier A
Start to develop
ULCP
>10kW@4.5K
2.5kW@4.5K/500W@2K
Helium CR
1959
Piston helium expander
Turbo helium expander
10kW@20K
Helium CR
40L/h Helium Liquefier B

## Slide 5
ULCPs are the indispensable core equipment for LS-Facilities
ULCPs and their related systems usually account for 1/4 of the investment and 1/2 of the space
More and more LSF need ULCP  LHC，ITER，E-XFEL , ESS，LCLS-II，KSTAR
1. Background：Demands – LS-Facilities

## Slide 6
High pressure GH2
LH2
The bottleneck of H2 energy utilization: transportation cost is too high
LH2: Best means for L-distance, L-scale, L-cost and Uh-purity Storage & Transportation
Industrial threshold level: 5 tons/day H2 Liquefier
1. Background：Demands – H2 Energy Utilization
Transportation distance [km]
Economic analysis of H2 transportation
Price [CNY]

## Slide 7
    ULCP is the key equipment for helium exploitation from NG
NG containing Helium or BOG
Pretreatment
(deacidification and dehydration)
Concentration
(60-90%)
Purification and liquefaction (99.999% -- >99.9999%)
External transportation
1. Background：Demands – Helium Exploitation

## Slide 8
4K CB
T.E.
HX
ULCP System composition
Val
Int Pur
2K CB
C.C.
VLP-HX
Val
Core Technologies
Equipment/system | Function | Core Technologies
T.E.（heavy load） | The only moving and cooling part of 4K system (4K heart) | Stability technology of heavy duty, low-T and high speed turbine machinery
C.C.（Large flow） | The only moving and cooling part of 2K system (2K heart) | 
Internal Purifier | Purification of contaminated helium (Liver detoxification) | High- low-T internal purification technology
System design and Integration | Overall system construction and control (brain command) | High- and high-reliability system design and integration technology
M.C.
CL & ORS
Control
1. Background：Core Technologies

## Slide 9
Contents
1. Background
2. Advances in Key Parts/Tech.
3. Advances in Systems
4. Conclusions & Prospects
Contents

## Slide 10
4KCB
T.E.
Int. Purifier
HX
Val
2K CB
C.C.
VLP-HX
Val
M.C.
CL & ORS
Concentration Device
（60%90% helium）
LHe user
SFHe user
Process Design
Source
（3% helium）
2. Typical Working Process of ULCP

## Slide 11
According to the requirements of CiADS for TS, supercritical He and superfluid He, 4kW@2K CP design and optimization has been completed.
H2 liquefaction process with liquefaction rate of 3800L/h and specific power consumption of 11.67kWh/kgLH has been completed.
Based on the demand for helium transportation, the process design and optimization of 3000 L/h helium liquefier was completed with the goal of liquefaction rate and specific power consumption.
3000L/h He Liquefier flow scheme
4kW@2K Superfluid He CP flow scheme
3000L/h H2 Liquefier flow scheme
2. Process Design: Main Work

## Slide 12
The optimal working point model of the throttle is established, and the optimal design method of the UL-CP is proposed
The He property library (especially the data at superfluid He temperature zone) invoking problem has been solved
OP integrated calculation model of hydrogen conversion and heat exchange have been established and implanted
Directly calling Hepak
Optimization method (relationship between T/P and Q/L at the high voltage side of the final HX)
Integrated calculation model of OP conversion heat transfer
2. Process Design: Technological Breakthroughs

## Slide 13
Development process
2. HL Expansion Turbines: Main Work
Input parameters
Detailed Design
Engineering design
Processing & manufacturing
experimental condition
Assembling & Testing
Input from process design result
Main parameters of rotor system
Rotor dynamics analysis
Bearing performance prediction model
Test rig for rotor orbit
Preliminary design of bearing -rotor system
Heavy load dynamic balancing machine
Air compressor
Bearing-rotor systems with different parameters
Test rig for bearing-rotor system dynamic balance
Rotor-bearing system stability test
Optimizing design parameters
Theoretical Research
Construction of test bench
Experimental Research
Bearing design calculation
Feedback

## Slide 14
D=45mm，P=11bar
P distribution of journal bearing
8孔
12孔
16孔
20孔
P distribution of thrust bearing
Waterfall diagram of gas bearing rotor speed increase test
Rotor dynamics analysis
Design, Rig and Test
2. HL Expansion Turbines: Main Work
Test Rig for H2 bearing

## Slide 15
Dimensionless Bearing Capacity Curved Surface
Relative Parameter | Air | H2 | He
Relative dimensionless flow factor (FF) | 1.0 | 1.8 | 2.9
Relative number of bearings (NOB) | 1.0 | 0.5 | 1.1
NOB：
Dimensionless FF：
The universal prediction method of static and dynamic load capacity of gas bearing is established and verified (Dimensionless Flow Factor and Number of Bearing)
Significance of this prediction method
Spreading the experience of air bearing to that of He and H2: improving economy and safety
The static P effect of H2 is between or higher than that of He and Air
2. HL ETs: Technological Breakthroughs
Dimensionless FF
NOB
Dimensionless Load Capacity

## Slide 16
 | CC1 | CC2 | CC3 | CC4
Ratio | 2.9 | 2.1 | 1.8 | 1.5
V/(rpm) | 12000 | 16000 | 21000 | 30000
Flow passage of each stage of CC
Scheme：higher work（7kW） 4 stages
Parameters：Compression Ratio，Rotary Velocity
Prototype of the 4th stage CC is developed（Vmax）
Axial magnetic bearing
Radial magnetic bearing
Key parts of the prototype
2. LF Cold Compressors: Main Work

## Slide 17
Test Rig, Process and Results
Maximum Speed：42010 rpm（120% design speed）
Rotary accuracy：14 μm
Test rig at RT
2. LF Cold Compressors: Main Work
Orbit
Loading
5 min
Stable & test
10 min
Ovrspd
2 min
Unload
2 min

## Slide 18
Structural optimization of main shaft
Magnetic bearing circuit board and control parameter setting
2. LF CCs: Technological Breakthroughs
The control system of MB is simplified and improved
The online adjustment and optimization of the control parameters of MB is realized
The problem of anti-strong current interference of bearings and sensors has been solved
Balance disc is set and rotor mass is decreased to reduce unbalance of the rotor
The winding mode of rotor sleeve is optimized to prevent deformation of the rotor at high speed (50mm80mm)

## Slide 19
System Scheme：
  Cold source：LHe  Flexible and efficient
  Flow process：3HX+Lair tank  Cold recovery
Key parts：
  HX: HT + Condensing & freezing separator
  Lair Tank：Setting a 5m filter for G-L separation
Multi-channel sleeve type (HX1)
Frost-containing finned tube type (HX2)
Sleeve type (HX3)
Lair tank with gas-liquid separation and liquid level measurement
Test CB
2. Internal Purifier: Main Work

## Slide 20
High- internal purifier process (utilization of Lair cooling capacity)
Liquefaction rate / cold helium flow vs. feed gas purity
2. Internal Purifier: Technological Breakthroughs
Purity of feed gas
Liquefaction Rate [L/h]
Sequence control process
The utilization process of Lair cooling capacity to make the refrigeration capacity stable has been proposed
Sequence control method for internal purifier has been mastered

## Slide 21
Contents
1. Background
2. Advances in Key Parts/Tech.
3. Advances in Systems
4. Conclusions & Prospects
Contents

## Slide 22
The 1st set of 300L/h domestic industrial He liquefier
& 2000L domestic LHe Dewar
Liquefaction Rate（L/h） | 309.6
Specific power consumption（kWh/L） | 1.36
3. System advances: 300L/h He Liquefier - Prototype

## Slide 23
3. System advances: 300L/h He Liquefier - Formal
300L/h industrial helium liquefier – formal type
Performance curve
Time [h]
LHe Volume in Dewar [L]
Liquefaction Rate（L/h） | 372.1
Specific power consumption（kWh/L） | 1.13

## Slide 24
3. System advances: 5t/d H2 Liquefier
The CB of 5t/d H2 Liquefier has been integrated and will be tested soon
3D Design of the CB
Length | 14.7 | m
Width | 6.0 | m
Height | 5.4 | m
Vacuum degree | 10-8 | Pam3/s

## Slide 25
>80K：Connected by axial movable flange with the main part (fixed)
80K-20K：Main part
<20K：Connected by upper flange with the outside
Skid-mounted distribution structure
3. System advances: 3000L/h LHe / 4kW@2K CR
T>80K Region 80K<T<20K Region T<20K Region
3000L/h / 4kW@2K / 18kW@4.5K CB mechanical design

## Slide 26
Contents
1. Background
2. Advances in Key Parts/Tech.
3. Advances in Systems
4. Conclusions & Prospects
Contents

## Slide 27
The core technologies of the series of 10kW CP represented by “HL-TE, LF-CC, Internal Purifier, and process design" have been conquered for the first time at TIPC of CAS and in China.
With the support of relevant government departments and enterprises, the R&D of the complete systems of the 10kW CP are being in progress
  3000 L/h Helium Liquefier  LS-Facilities, Helium resource extraction
  5 t/d H2 Liquefier  2  H2 Energy Utilization
  4 kW@2K Superfluid Helium Cryo-plant  LS Facilities
4. Conclusions and Prospects：Conclusions

## Slide 28
  With the joint support of TIPC and Zhongshan City, Zhongshan Institute of Advanced Cryogenics (ZIAC) was established to build a large cryo-plants development platform and carry out research on the high efficiency, long life and application of ULCP
System Bld
Key Tech Bld
Complex Bld
H2 Bld
4. Conclusions and Prospects: Prospects

## Slide 29
Thank you for attending!