## Slide 1
Xiangyi Cui (崔祥仪)
On behalf of the PandaX Collaboration
PandaX-4T - A Multi-Tonne Liquid Xenon Detector for Dark Matter and Neutrino Physics
AFAD2023, Melbourne

## Slide 2
Dark Matter Direct Detection
WIMP
Ionization
Light
Phonons/heat
AFAD2023, Melbourne

## Slide 3
PandaX Collaboration
AFAD2023, Melbourne

## Slide 4
China JinPing Underground Laboratory – CJPL
CJPL-I
CJPL-II
  Deepest (6800 m.w.e )
  Horizontal access
  Muon rate: 1 count/week/m2
AFAD2023, Melbourne

## Slide 5
Dual Phase Liquid Xenon TPC
Purity liquid xenon target, high light & charge yield;
Good ER/NR separation by S1&S2;
3D reconstruction reject external background;
AFAD2023, Melbourne

## Slide 6
Particle and Astrophysical Xenon Experiments
PandaX-I, 120 kg
operation
PandaX-II, 580 kg operation
Collaboration formed
2009.3
2014.5-10
2016.7-2019.7
2019.8
PandaX-4T moved to CJPL-II
2021.4
PandaX-4T
Commissioning
Ongoing
2021.11
PandaX-4T Run1
PandaX-xT
AFAD2023, Melbourne

## Slide 7
PandaX-4T Overview
AFAD2023, Melbourne

## Slide 8
Cryogenics
Adjust Coldhead
temperature
Loop1 Maintenance
Loop2 In
Parameters | Heating load (No purification) | Maximum Cooling Power | Filling/Recuperation flow rate | Outer Vacuum
Value | ~50 W | ~580 W | ~1 ton/day | <2E-4 Pa
JINST 16 P07046 (2021)
Cryogenics
Purification
AFAD2023, Melbourne

## Slide 9
Purification system
Ref. the maximum drift time ~ 840 µs
Low Outgassing
High flow rate
NEXT
AFAD2023, Melbourne

## Slide 10
Distillation System
Structured packing
M-T diagram for Kr removal
Distillation method for the LXe intrinsic background Kr&Rn removal;
~106 reduction factor for Kr removal with 10 kg/h;
Reversed operation mode working for Rn removal;
JINST 16 T06007 (2021)
AFAD2023, Melbourne

## Slide 11
Distillation
NEXT
 |  | PandaX-4T | Upgraded
Flow rate [kg/h] | Kr | 10 | 30
 | Rn | 56.5 | 856
Reduction factor | Kr | 106 | 108
 | Rn | 2.2 | 4.4
Run0
Set4
Run0
Set5
Run1
Preliminary
Preliminary
AFAD2023, Melbourne

## Slide 12
TPC conditions
 | Set1 | Set2 | Set3 | Set4 | Set5
Gate(kV) | -4.9 |  | -5 | -5 | 
Cathode (kV) | -20 | -18.6 | -18 | -16 | 
AFAD2023, Melbourne

## Slide 13
PMT Arrays
Bottom PMT arrays
169 top + 199 bottom R11410-23 3-inch PMTs, with the average gain of 5.5×106;
LED calibration every week;
 |  | R11410 | R12699
Time Response [ns] | Rise Time | 5.5 | 1.2
 | Transit Time | 46 | 5.9
Radioactivity [mBq/pc] | Co-60 | 1.16±0.72 | 0.00±0.04
 | Th-232 | 4.33±2.16 | 0.13±0.17
 | U-238 | 26.29±16.90 | 0.00±0.62
R12699 2-inch PMTs with 4 independent anode readout;
Better time response for better waveform build;
Lower radioactivity;
NEXT
AFAD2023, Melbourne

## Slide 14
Electronics
NEXT
V1725 Digitizer, 250 MS/s;
Self-trigger mode: read out pulses above 20 ADC (~ 1/3 PE);
Custom-developed: 14-bit, 500MS/s
Higher sampling rate;
Accept out-trigger mode;
AFAD2023, Melbourne

## Slide 15
Calibration
Gaseous source injection panel
Calibration tubes
Calibration source | Position
83mKr/220Rn | Injected from gas panel
241Am-Be | Calibration tubes
D-D neutron | Beam pipe
D-D generator
AFAD2023, Melbourne

## Slide 16
Detector Response
220Rn
D-D
ER leak ratio (below NR median curve) is 0.43%±0.18%;
Efficiencies separately determined from ER or NR calibration data are all consistent;
AFAD2023, Melbourne

## Slide 17
Background
Expected below-NR-median events: 9.8 (0.6) evts
ER (Rn+Kr+Material+Tritium) background dominated in the selection region;
Background per unit target is improved from PandaX-II by 4 times (<10 keV);
AFAD2023, Melbourne

## Slide 18
PandaX-4T first commissioning Result - WIMPs
1058 candidates (expected 1054±39), 6 below NR median curve (expected 9.8±0.6);
Sensitivity improved from PandaX-II final analysis by 2.9 times (30 GeV/c2);
PRL 127, 261802 (2021)
0.63 tonne·year
AFAD2023, Melbourne

## Slide 19
Neutrino Physics
Solar Neutrino – 8B
Neutrino double beta decay – 136Xe
PRL 130, 021802 (2023)
Research 2022, 9798721 (2022)
AFAD2023, Melbourne

## Slide 20
NEXT - PandaX-xT
Majorana neutrino
> 2 MeV
Dark Matter
1 keV – 10 keV
Astrophysics neutrino < 300 keV
  With >30 tonne liquid xenon in the sensitive volume;
  Decisive test on WIMP and key test on Dirac/Majorana neutrino;
AFAD2023, Melbourne

## Slide 21
Summary and outlook
PandaX-4T is one of the new generation multi-tonne xenon experiments (operation until 2025)；
Intense searches for various types of physics, including DMs and neutrinos;
In parallel, the collaboration is developing the plan for the next generation experiment at CJPL;
Highly welcome new collaborators!
AFAD2023, Melbourne