## Slide 1: Commissioning of The first southern hemisphere’s first X-band radio-frequency test facility at the University of Melbourne.
Matteo Volpi on behalf of the X-LAB group
The Asian Forum for Accelerators and Detectors (AFAD-2023)

## Slide 2
X-band Laboratory for Accelerators and Beams (X-LAB)
  A new laboratory is under commissioning at the University of Melbourne (UoM) to build a next generation compact light source.
    First high-power, high-frequency accelerator laboratory in the South Hemisphere.
    Testing high gradient structure prototype and RF components for CLIC
    Ultra-precision manufacturing
    Design and develop more widely available high quality x-ray sources
  This project will provide local researchers and students with an opportunity to make significant advances in accelerator design
  Excellent potential for applications in medical radiation therapy and beyond

## Slide 3
At the heart of the project is the X-band high power equipment including modulator and klystron (left) feeding rf power to two copper accelerating structures (right). An electron source will also enable acceleration of electron beams.
CERN layout before the shipping

## Slide 4: Conditioning CLIC prototype structures (TD24)
CLIC structures high power tested so far.
Facilities need to be able to predict breakdown to ensure reliability of operation while in collider applications the large number of rf structures also require reduced likelihood of breakdown. Each RF breakdown causes a destructive sideways kick to the particle bunches. This is why accelerating structures are conditioned - or ‘broken in’ - before operation. The process of conditioning requires a variation of input pulses as gradient and pulse width to ensure reliability of operation to attain the lowest possible breakdown rate.
(ns)
TD24 structure so far reached 40.45 MW (97.9 MV/m)

## Slide 5: 2022 Melbourne Bunker
Previously used for 35 MeV betatron
~70m2: Space for x-band linac and medical applications
  Refurbishing scheduled for the next months

## Slide 6: 2023: Commissioning Melbourne Bunker
Previously used for 35 MeV betatron
~70m2: Space for x-band linac and medical applications
  Refurbishing scheduled for the next months
Vacuum Rack
Total power up to ~50MW
2x Toshiba 6MW klystron
2x Scandinova Modulators
Nominal Rep Rate 400 Hz
NI-PXI Crate
LLRF Rack
Pulse Compressors
Modulator C
Modulator D

## Slide 7: MeL-BOX Layout
Schematic of the X-lab setup for experimental structure testing and conditioning CLIC prototype structures.
Klystron Conditioning Layout
UoM
Phase I
Control room
KLY C
KLY D
KLY C
KLY D

## Slide 8: Klystron Conditioning Layout
3D load 3T N8 (~25dB)
Pump: IP_KLY_C
KLY C
Pump: IP_HYB_3
3D load CERN N5 (~30dB)
KLY_IN_C
PKI_C
PKR_C
RF widow
Gage: Load_3 B1
Gage: Line_3 A1
Pump: IP_PC_3
Pump: IP_LINE_3
KLY_IN_D
PKI_D
PKR_D
KLY D
Klystron widow
Klystron widow
RF widow

## Slide 9
  New RF window; designed for 4/5us pulse width up to 20MW
  S11 ; S22~-25 dB attenuation
  S12 ~ 0.05 dB transmission
  Vacuum : ~10-10 mbar
High Power RF Window

## Slide 10
  Pulse width up to 5us
  LCW ~ 80 l/m
  Max repetition rate 400Hz
  Nominal Voltage 950 Volts
    To stabilize the power the klystron is pulsing at the nominal voltage.
    The LLRF (low-level radio frequency) controls power by adjusting the input power to the SSA (solid-state amplifier)
Klystron Conditioning

## Slide 11: Read-out system/Interlocks
RF window vacuum
3D Load vacuum
Klystron vacuum
Power ramp
  Klystron conditioning is limited by the 3D loads designed for CLIC pulses (~200ns)
    Next week we will install the 1m long loads designed for 4/5 us pulse width and 50MW power.
  Interlocks at this stage:
    Reflected power
    Vacuum
Klystron input power
Reflected power
Klystron output

## Slide 12: Gain curves
Klystron C 150ns pulse width
Klystron D 100ns pulse width

## Slide 13
X-band for Industrial and medical technologies
Phase II
See Scott W. talk: Beamline simulations for the University of Melbourne X-LAB

## Slide 14
Local Manufacturing
Australian National Fabrication Facility (ANFF): manufactured a W90 to waveguide adaptor
  “This project has been a good chance to review some of our processes and equipment gaps.”
They have been using monocrystal diamond tooling
  surface roughness ~Ra 7nm (best measured so far)
  tolerances within 1µm
Be able to make disc? Not sure, but that our overall aim for the future is to have that capability.
In a few months they will make a disk
GOAL: try to build a low beta structure.

## Slide 15: Conclusion and future plan
A multi-million-dollar X-band equipment has been commissioned at the UoM to serve as the central infrastructure for further development in the new X-Lab.
This project will shift Australia’s long-standing position as an excellent user of particle accelerators, to a world-leading developer of this cross-cutting technology.
  14th of February; first high power X-band pulses on the Sothern Hemisphere
Both klystron have been conditioned up to their maximum power with ~200ns pulse width
  Welcome to visit the facility!
    Help and support are more than welcome !

## Slide 16: Dark current and radiation in high-gradient RF structures
High surface electric fields lead to spontaneous emission of electrons from the material surfaces.
Field emitted electrons can be captured by the EM fields and be accelerated throughout the structures, causing the so-called dark currents.
If these electrons become energetic enough they can also produce ionizing radiation when colliding with material walls.
Curtesy of David Caballero
e- energy
TD24 structure

## Slide 17: Radiation Simulation
A simulation of the bunker area has been performed with FLUKA software. The simulation includes:
  Two high gradient structures with upstream, downstream and later electron sources
  Bunker geometry including old electron beam holes and emergency exit (weak point)
    The bunker area was hosting a 35 MeV electron beam betatron
  Lead shielding around the structures:
    Downstream lead bricks around the faraday cup
    Two lead walls
  20 cm thick chicane wall plus interlock gate.
20MeV e-
Downstream
Faraday Cup
1MeV e-
Upstream
0.5MeV e-
Structure
Bunker
Structures
Bunker Geometry
Emergency exit
z
x
Beam line
x
y
z
x

## Slide 18: DOSE-EQ
Soil
Soil
Dark Matter Lab
DOSE-EQ above the annual threshold 1mSv
DOSE-EQ > 1mSv/year
No limits applied
Setup Summary:
  20 MeV
  100ns flat top
  0.5 mA dark current
  200 Hz repetition rate
  2000 working hours per year, (40h/week x 50 weeks)
  Shields:
    Lead bricks around downstream faraday cup
    Wall bricks around the structures

## Slide 19: Structure production flow

## Slide 20: MeL-BOX Layout
x6 FPGA IQ demodulation 400-MHz AC (228MSPS ADCs)Phase and amplitude needed for reliable line/phase switching.
x6:3 FPGA IQ demodulation 400-MHz AC (1600MSPS ADCs)  Most interesting signals for BD physics.
x4:2 Faraday Cups (250MSPS ADCs)  Used to interlock the system and are interesting for high gradient physics.
x6 Log detectors ~50MHz Bandwidth, 45dB dynamic range (250MSPS ADCs)  Used for interlocking the system.
DUT
DUT
FPGA IQ demodulation slow ADCs
FPGA IQ demodulation fast ADCs
Faraday cups
Log detectors