## Slide 1: ILU RF electron accelerators for e-beam and X-ray applications.
Aleksandr Bryazgin
Budker Institute of Nuclear Physics
Novosibirsk, Russia

## Slide 2: ILU-8 in Local Shield
Energy 0.8-1 MeV
Av. Current 0-20 mA
Pulse current 0-500 mA
Main features of ILU accelerators
Compact
Self-excitation
No insulation and gas systems
Pulse
GI-50
Pulse duration 800 mks
Pulse repetition 1-50 Hz
RF frequency 175 MHz
Dim D800x800 mm

## Slide 3: Features of ILU accelerators
Not expensive RF tube GI-50 with lifetime>7000 hour (~10000 USD) and pulse power 2 MW.
Soft requirements for temperature stabilization cooling water ~5-10 degrees of Celsius.
Fast start: not necessary warming of cavity, just fast warming of filaments.
Master-generator
Amplifier
Cavity
Amplifier
Cavity
Positive feedback
Master-generator
Tube GI-50A
Usual linac
ILU accelerator

## Slide 4: Cavity voltage and beam current for one cavity.
CW
Pulse
No energy looses
here
No energy looses
here
Pulse Linear Accelerator PLA=ИЛУ (ILU) in Russian
Ibeam=10 mA
Ibeam (average)=10 mA
Energy looses in cavity always
Efficiency lower
Efficiency higher

## Slide 5: 4-sided cable irradiation
Beam extraction device for 4-sided irradiation
allows to increase
beam usage efficiency
comparing with
2 sided irradiation
No cable twist

## Slide 6: Accelerator ILU-8 in local shielding

## Slide 7: ILU-10
Energy 4-5 MeV
Av. Current 0-10 mA
Pulse current 0-400 mA
Pulse duration 500 mks
Pulse repetition 1-50 Hz
RF frequency 115 MHz
Dim. D1280x1480 mm

## Slide 8: ILU-10 in Novosibirsk pharmaceutical plant 2013

## Slide 9: ILU-10 in Novosibirsk pharmaceutical plant 2013

## Slide 10: ILU-10 in Novosibirsk pharmaceutical plant 2013

## Slide 11: Centre of radiation technologies in Budker Institute (started 2014)

## Slide 12: Centre of radiation technologies in Budker Institute (started 2014)

## Slide 13: Centre of radiation technologies. Conveyor load zone.

## Slide 14: Centre of radiation technologies. Control cabinet.

## Slide 15
Sterilization center based on ILU-10 in Semipalatinsk
nuclear test site (STS) in Kazakhstan.

## Slide 16: ILU-10 in Kaitech university, Korea
BINP
+

## Slide 17: Increasing power of ILU-10
= 1.77 MW
Rshunt=7 Mohm, U=5 MV
Ploss_av=1770*0.025=44.25 kW
RF power of 1 generator – 2 MW of pulse power or 50 kW of average power for duty cycle 0.025 (F=50 Hz, Tpulse= 500 mkS)
Number generators | Average beam power for 5 MeV (kW)
1 | 0
2 | 50
3 | 100
4 | 150

## Slide 18: Medical sterilization and food irradiation markets required more energy and power.
Food irradiation requirements
10 MeV E-beam → small power
X-ray 5 MeV → huge power (conversion rate ~8%)
X-ray 7.5 MeV (USA, Indonesia, Canada, India, Korea) → high power (conversion rate~13%)

## Slide 19: New multi-cavity ILU accelerator.
One cavity
Multi-cavity
Chart: Efficiency on Number of cells
8MW | 0.556 | 0.65 | 0.71 | 0.75 | 0.78 | 0.8 | 0.82

## Slide 20: ILU-14 10 MeV 100 kW
Operating frequency, MHz | 176 | Full efficiency, % | 26
Electron energy, MeV | 7,5-10 | Modulator pulse duration, μs | 500
Average beam power, kW | 100 | Repetition rate, Hz | Up to 50

## Slide 21: New multi-cavity ILU accelerator.
In operation from 2014 in Moscow

## Slide 22: ILU-14 for food irradiation in Vietnam

## Slide 23: ILU-14 for food irradiation in Vietnam

## Slide 24: ILU-14 for food irradiation in Vietnam

## Slide 25: Shorter version – ILU-12
5 MeV 60 kW
7.5 MeV 40 kW
4 cavities
Possible upgrade to ILU-14

## Slide 26: X-ray converter
E(MeV) | Ta thickness | 60 deg | 360 deg
7.5 | 0.9 | 13,2% | 16,9 %
5 | 0,7 | 8,3% | 12%
Conversion rate X/ray/Ebeam power

## Slide 27
Thank you for your attention