## Slide 1: Development of high-energy irradiation accelerators in China
Jiaru Shi
Tsinghua University
On behalf of the linac team

## Slide 2: Outline
Introduction to the irradiation accelerators
Backward traveling-wave (BTW) linac
Development of a 10-MeV, 24-kW BTW linac
Other activities on 10-MeV high-power irradiation

## Slide 3: accelerator technology for irradiation & sterilization
Damage to the molecular of the harmful organism. To control insects, parasites and pathogens, reduce spoilage.
Inhibit sprouting, delay ripening and extend self-life for certain farm produce.
Apply to irradiation processing of food, medical product, quarantine treatments and etc.

## Slide 4
Low Energy
  <300keV
  E-beam curing
Middle Energy
  0.3-5MeV
  Cross-linking of polymers, for cable / rubber …
High Energy
  5-10MeV
  Sterilization …Food irradiation

## Slide 5: Application fields
Medical products, Medicine, Mails……Sterilization

## Slide 6: Application fields
Food irradiation

## Slide 7: Application fields
Irradiation phytosanitary treatment

## Slide 8: Excellence of E-Beam system
No environmental pollution.
Quick processing, high efficiency.
Do not open the packing case, so it can get across quickly and safely.
No toxicity or remains. Do not add any chemical reagent, so no original element and quality of products is influenced.

## Slide 9: Linac
Irritation E-beam facility
  Dynamitron/Linac/Rhodotron/Ridgetron/Fantron
LINAC
  Standing wave/Traveling Wave/Backward Traveling Wave
Parameters
  10MeV （most common for e-beam）
  Beam power (higher is better: linac 20kW, rhodotron ~100kW)
[1] 陈怀璧等； 返波型行波电子直线加速结构的理论研究

## Slide 10: Introduction of BTW structure
BTW structure
  High-shunt impedance (~ Optimized shape)
  Short filling time (~Traveling wave)
 | Shunt impedance | Filling time | AFC | Reflection from input | Peak surface field
Disk-loaded TW | Low | Short | No | Low | Low
Bi-periodic SW | High | Long | Yes | High | High
BTW | High | Short | No | Low | High

## Slide 11: BTW structure
Cells coupled through coupling holes
  Beam-pipe cut off
  Easy for tuning a structure
  RF focusing
Power flow opposite direction to the beam
  High efficiency
  Easy for cooling the input coupler
Pout
Pin
Beam

## Slide 12: History of BTW 10MeV-20kW
Ebeam:
  Energy： 10MeV
  Peak current： 300mA
  Average power： 20kW
Accelerator tube:
  BTW type
  length：1.5meter
RF source:
  5MW/45kW klystron @ 2856MHz
Cooling jacket, Solenoid, Pumping port

## Slide 13
Standing wave
Back wave
System integration (Nuctech)

## Slide 15
E-beam irradiation integrated processing center
Case 2 (Shanghai,2012)

## Slide 16: System operation
2013 Sept, first set in Shanghai, operated for more than 50,000 hour until now;
2014~2021, in Shanghai, Guangzhou, Chongqing and etc., export to Mexico, Italy and Pakistan, with more than 20 set and all operating stably.
Mexico
Italy
Pakistan

## Slide 17
Mail sterilization System (2002)
Products
Mail sterilization system (2008)
Mobile sterilization system (2005)
5MeV/2kW mail sterilization
Lower Power
Notes: 17
17

## Slide 18: Problem of Beam breakup (BBU)
BBU experiment on 10MeV BTW linac
To observe BBU, sweeping the beam current and pulse width
Current larger than 260mA will result in BBU
Average Power Limited to 20kW
BTW linac system
Pulses of BBU (Orange gun emission，green Output of linac)
Pulse width vs beam current

## Slide 19: Beam breakup (BBU) study
Le Duff J. Beam break up[R]. Paris-11 Univ., 91-Orsay (France). Lab. de l'Accelerateur Lineaire, 1985.
ebeam
Normal
BBU
管壁
Loss
Phenomenon
  The tail of pulse will be lost. The beam current is limited.
Physics mechanism
  The following electron will be deflected by the wake field generated by the previous beam.
  Collective beam instability.
  m=1 transverse wake field
  (HEM11 mode) can be amplified by the beam itself.

## Slide 20: Physics study and new linac design
Beam breakup mechanism
Various beam experiments on 1020 linac to analyze causes of BBU
  Dose distribution after BBU
  Beam spot after BBU
  Microwave signal after BBU
  ……
New linac design
  Optimize bunching
  Optimize coupler
  …………

## Slide 21: Timeline: low-power test
Development of new Tube in 2020
RF meas. in Tsinghua Acc Lab
OLD design
NEW design

## Slide 22: Timeline: high-power test
2020 September, fabrication complete
2020 Nov- 2021 Jan，High-power test at NUCTECH

## Slide 23: 10MeV 24kW BTW
Full 24kW Beam Power Output！（2020.12.21）
>300mA without BBU
The new design solve the BBU problem!
Rep frequency: 625pps
Pulse current: 300mA
Pulse width： 12.5us
Energy: 10.5MeV
Ave current: 2.4mA
Beam power:
25.2kW

## Slide 24: Parameters comparison
 | Old | New | 
Klystron | 5MW 45kW | 5MW 45kW | 
Pulse current | 260mA | 310mA | 
Beam energy | 10MeV | 10MeV | 
Rep. frequency | 650Hz | 625Hz | 650Hz
Current width | 12us | 12.5us | 12.5us
Average current | 2mA | 2.4mA | 2.4mA
Capture rate | 30% | 35% | 35%
Efficiency | 45% | 53% | 53%
Beam power | 20kW | 25.2kW | 26kW

## Slide 25
10MeV 24kW system upgrade
More than 10 sets of 24kW system in the pipeline
Two finished in 2022

## Slide 26
Ridgetron prototype @ CIAE
Energy 9.8MeV
Power 56kW
http://www.ciae.ac.cn/newsContent.jsp?RID=3627
Result of 2022.12
CIAE: China Institute of Atom Energy (in Beijing)
Picture from: N Hayashizaki, et al. NIMA Volume 427, Issues 1–2, 1999,

## Slide 27
10MeV linac systems have been developed and widely installed in China
10MeV-24kW systems successfully developed in Tsinghua University. Been operating for ~1 year. Beam-power and Efficiency upgrade
Ridgetron (10MeV-50kW) prototype developed in CIAE in China
Summary

## Slide 28
Thanks for listening！
E-mail：XXX XXX