## Slide 1
Radiotherapy LINAC Breakdowns in Low- and Middle-Income Countries
Greg Peiris
gpeiris@student.unimelb.edu.au
  13th Apr 2023
Notes: For the next few moments I will illustrate the need for reliable and affordable cancer care throughout the world, but especially in LMICs
And then outline the ways we plan to combat this issue as physicists

## Slide 2: Cancer
The Great Equalizer
Cancer does not discriminate based on income or status, place of birth or age
Notes: Some have called cancer the “Great Equalizer”. This name comes from the fact that cancer does not discriminate based on income or status, place of birth or age. While this sentiment is admirable, it is far from the truth. Cancer is not just the act of getting cancer, it is also the diagnosis, the equipment needed for treatment, the genetic history and a multitude of other factors. And when all of these are considered, it is the people in Low- and Middle-Income Countries that are most affected by the “Great Equalizer”. Within the next 10 years, it is projected these countries will bear up to 75% of cancer related deaths globally and as it stands only 5% of global resources spent on them.

## Slide 3: Cancer
The Great Equalizer …or is it?
Cancer does not discriminate based on income or status, place of birth or age
Cancer is not just the cancer:
  Diagnosis
  Equipment needed for treatment
  Genetic history
  Lifestyle and social factors, etc.
75% of deaths in Low and Middle Income Countries (LMIC) by 2030
Notes: Some have called cancer the “Great Equalizer”. This name comes from the fact that cancer does not discriminate based on income or status, place of birth or age. While this sentiment is admirable, it is far from the truth. Cancer is not just the act of getting cancer, it is also the diagnosis, the equipment needed for treatment, the genetic history and a multitude of other factors. And when all of these are considered, it is the people in Low- and Middle-Income Countries that are most affected by the “Great Equalizer”. Within the next 10 years, it is projected these countries will bear up to 75% of cancer related deaths globally and as it stands only 5% of global resources spent on them.

## Slide 4: Cancer
High Income Country facilities (above)
Low and Middle Income facility (right)
The Great Equalizer …or is it?
Cancer does not discriminate based on income or status, place of birth or age
Cancer is not just the cancer:
  Diagnosis
  Equipment needed for treatment
  Genetic history
  Lifestyle and social factors, etc.
75% of deaths in Low and Middle Income Countries (LMIC) by 2030
Cancer care in LMICs is very limited
  Long delays and wait times
Notes: This disparity is due to the differences in cancer care.
Unfortunately, it is rarely readily available and long wait times cause tumours to advance to higher stages before diagnosis. Sometimes this means grotesquely large tumours where surgery is no longer a safe option. The environmental and socio-economic conditions these countries have means that state-of-the-art technology doesn’t survive long.

## Slide 5: Radiation Therapy
Why is it perfect for Low-and Middle-Income Countries?
Radiation Therapy, or Radiotherapy (RT), is an effective method of cancer treatment
Compact machines
Short treatment times and often no hospital stay needed
Notes: This is particularly unfortunate, since radiotherapy has significant advantages for all nations, especially LMICs. The process is non-invasive and 40% of all successfully treated cancer cases involve radiation therapy. The machines used to deliver RT are compact and a lot safer than the old Cobalt 60 or Cesium 137 machines. Treatment sessions can be as short as 10mins and patients don’t need to stay in the hospital- continuing to go about their daily life if they feel up to it. And even though the initial cost of a radiotherapy machine might be high, they will last for quite some time… or so we thought.

## Slide 6: Radiation Therapy
Why is it not perfect for Low-and Middle-Income Countries?
Radiation Therapy, or Radiotherapy (RT), is an effective method of cancer treatment
Compact machines
Short treatment times and often no hospital stay needed
Rather expensive machines
Low-and Middle-Income Countries (LMICs) at a disadvantage
RT machines breakdown frequently in LMICs due to harsh conditions
Notes: The radiotherapy linear accelerator is an intricate bit of engineering that breaks down in the harsh conditions of low and middle income countries. As it stands, the availability of RT machines is quite low. This figure here

## Slide 7: Radiation Therapy
Why is it not perfect for Low-and Middle-Income Countries?
Radiation Therapy, or Radiotherapy (RT), is an effective method of cancer treatment
Compact machines
Short treatment times and often no hospital stay needed
Rather expensive machines
Low-and Middle-Income Countries (LMICs) at a disadvantage
RT machines breakdown frequently in LMICs due to harsh conditions
Figure 1: Radiotherapy LINAC availability by population. Created using DIRAC Database and IAEA Data
Notes: The radiotherapy linear accelerator is an intricate bit of engineering that breaks down in the harsh conditions of low and middle income countries. As it stands, the availability of RT machines is quite low. This figure here shows a significant lack of radiotherapy machines through sub-Saharan Africa, subcontinent asia, south east asia and central America. A breakdown in one of these countries means patients have to travel large distances, sometimes another country to get treated.
But what exactly is the radiotherapy machine?

## Slide 8: Radiotherapy LINACs
How do we deliver radiotherapy?
Notes: The Radiotherapy Linear Accelerator or LINAC can be broken down into three main components: The radiofrequency power generation by use of a klystron or magnetron depending on the machine,
the treatment and dosage of X-rays delivered to the patient, and the accelerating components

## Slide 9: Radiotherapy LINACs
How do we deliver radiotherapy?
Notes: The Radiotherapy Linear Accelerator or LINAC can be broken down into three main components: The radiofrequency power generation by use of a klystron or magnetron depending on the machine,
the treatment and dosage of X-rays delivered to the patient, and the accelerating components

## Slide 10: Radiotherapy LINACs
How do we deliver radiotherapy?
Power Supply
Notes: The Radiotherapy Linear Accelerator or LINAC can be broken down into three main components: The radiofrequency power generation by use of a klystron or magnetron depending on the machine,
the treatment and dosage of X-rays delivered to the patient, and the accelerating components

## Slide 11: Radiotherapy LINACs
How do we deliver radiotherapy?
Accelerating Electrons
Power Supply
Notes: The Radiotherapy Linear Accelerator or LINAC can be broken down into three main components: The radiofrequency power generation by use of a klystron or magnetron depending on the machine,
the treatment and dosage of X-rays delivered to the patient, and the accelerating components

## Slide 12: Radiotherapy LINACs
How do we deliver radiotherapy?
Power Supply
Treatment with X-Rays
Accelerating Electrons
Notes: The Radiotherapy Linear Accelerator or LINAC can be broken down into three main components: The radiofrequency power generation by use of a klystron or magnetron depending on the machine,
the treatment and dosage of X-rays delivered to the patient, and the accelerating components

## Slide 13: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
Notes: To illustrate this, I want to show you the results of two recently published papers. One that compares radiotherapy machine breakdowns in the UK to ones in Nigeria and Botswana by Lawrence Wroe. And another paper that looks at breakdowns all through Indonesia by myself and our research group.

## Slide 14: Failure Modes
19
Is it that much worse in LMICs?
Wroe
Peiris
6
2
6
LMICs v HICs [Wroe Data]
RT LINACs in LMICs fail more often than those in HICs in 9 out of 12 categories.
Notes: Lawrence Wroe first split the machine into 12 subcategories for where breakdowns can occur and showed that LMICs fail more often in 9 out of the 12. Of note…

## Slide 15: Failure Modes
19
Is it that much worse in LMICs?
Wroe
Peiris
6
2
6
LMICs v HICs [Wroe Data]
RT LINACs in LMICs fail more often than those in HICs in 9 out of 12 categories.
Notes: These 4 subcategories failed far more frequently in LMICs compared to HICs.

## Slide 16: Failure Modes
19
How do LINACs break in HICs?
Wroe
Peiris
6
2
6
< 5mins
5mins < x < 60 mins
> 60 mins
Minor Faults
Debilitating Faults
Workflow Interrupt -ing Faults
Notes: These 4 subcategories failed far more frequently in LMICs compared to HICs.

## Slide 17: Failure Modes
19
How do LINACs break in HICs?
Wroe
Peiris
6
2
6
Notes: These 4 subcategories failed far more frequently in LMICs compared to HICs.

## Slide 18
Bremsstrahlung converts electrons to X-Rays
Tungsten has good thermal properties and high atomic number
Multi-leaf Collimator
What is the Multi-leaf Collimator?
Notes: Once the accelerated through the LINAC, electrons strike a tungsten target and they are converted into x-rays via bremsstrahlung.

## Slide 19
Shapes the X-Ray beam into the tumor’s shape using tungsten leaves
Aims to maximise dose to tumor and minimise to Organs
Bremsstrahlung converts electrons to X-Rays
Tungsten has good thermal properties and high atomic number
Multi-leaf Collimator
What is the Multi-leaf Collimator?
Notes: Once the accelerated through the LINAC, electrons strike a tungsten target and they are converted into x-rays via bremsstrahlung.
These are then collimated using the multi-leaf collimator to the shape and size of the tumor using tungsten leaves. These leaves can move in real time as the gantry rotates about the patient.

## Slide 20
Is the clinical standard and used on most LINACs
Treatment Planning Systems are used to optimise configuration
Bremsstrahlung converts electrons to X-Rays
Tungsten has good thermal properties and high atomic number
Shapes the X-Ray beam into the tumor’s shape using tungsten leaves
Aims to maximise dose to tumor and minimise to Organs
Multi-leaf Collimator
What is the Multi-leaf Collimator?
Notes: Once the accelerated through the LINAC, electrons strike a tungsten target and they are converted into x-rays via bremsstrahlung.
These are then collimated using the multi-leaf collimator to the shape and size of the tumor using tungsten leaves. These leaves can move in real time as the gantry rotates about the patient.
It is currently used in many medical treatment techniques including Intensity Modulated Radiotherapy, Volumetric Modulated Arc Therapy and 3D Conformal Radiotherapy
The ultimate aim is to maximise the amount of dose that goes into the tumor while sparing the vital organs such as the optic nerve or spine

## Slide 21
Shapes the X-Ray beam into the tumor’s shape using tungsten leaves
Aims to maximise dose to tumor and minimise to Organs
Is the clinical standard and used on most LINACs
Treatment Planning Systems are used to optimise configuration
Has lots of moving parts and components
Bremsstrahlung converts electrons to X-Rays
Tungsten has good thermal properties and high atomic number
Multi-leaf Collimator
What is the Multi-leaf Collimator?
Notes: Once the accelerated through the LINAC, electrons strike a tungsten target and they are converted into x-rays via bremsstrahlung.
These are then collimated using the multi-leaf collimator to the shape and size of the tumor using tungsten leaves. These leaves can move in real time as the gantry rotates about the patient.
It is currently used in many medical treatment techniques including Intensity Modulated Radiotherapy, Volumetric Modulated Arc Therapy and 3D Conformal Radiotherapy
The ultimate aim is to maximise the amount of dose that goes into the tumor while sparing the vital organs such as the optic nerve or spine.
It is this component that breaks down most often in LMICs and recently we’ve found it to be causing some grief in HIC as well.

## Slide 22: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
6
1
3
1
1
1
1
LMICs [Indonesian Data]
Data collected all through Indonesia spanning the years 2000 through 2019. Total of 14 Hospitals in the study. Collected logbooks, data records and a survey of the medical physicists.
Notes: Using the lettered categories mentioned earlier we divided the faults to get a better sense of what kind of MLC faults dominated the Indonesian data set. And though B faults were grater in number, they only made up a fraction of the downtime. Debilitating faults, type C faults, contributed to 95% of the total downtime. Compare this to machines in Oxford, where an MLC was down for longer than an hour only 23 times.

## Slide 23: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
LMICs [Indonesian Data]
<5 min faults are very low in LMICs
Notes: Using the lettered categories mentioned earlier we divided the faults to get a better sense of what kind of MLC faults dominated the Indonesian data set. And though B faults were grater in number, they only made up a fraction of the downtime. Debilitating faults, type C faults, contributed to 95% of the total downtime. Compare this to machines in Oxford, where an MLC was down for longer than an hour only 23 times.

## Slide 24: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
LMICs [Indonesian Data]
- 59.02% of Mechanical faults are due to the MLC
Notes: Using the lettered categories mentioned earlier we divided the faults to get a better sense of what kind of MLC faults dominated the Indonesian data set. And though B faults were grater in number, they only made up a fraction of the downtime. Debilitating faults, type C faults, contributed to 95% of the total downtime. Compare this to machines in Oxford, where an MLC was down for longer than an hour only 23 times.

## Slide 25: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
LMICs [Indonesian Data]
- 57.14% of replacements are due to the MLC
Notes: Using the lettered categories mentioned earlier we divided the faults to get a better sense of what kind of MLC faults dominated the Indonesian data set. And though B faults were grater in number, they only made up a fraction of the downtime. Debilitating faults, type C faults, contributed to 95% of the total downtime. Compare this to machines in Oxford, where an MLC was down for longer than an hour only 23 times.

## Slide 26: Failure Modes
Is it that much worse in LMICs?
Wroe
Peiris
19
6
2
6
LMICs [Indonesian Data]
How to improve uptime of the machines | No. of Medical Physicists
Better training of hospital staff | 13
Better availability of vendor engineers | 11
Easier access to spare parts | 11
More robust LINAC which breaks less often | 4
Frequent communication between client and vendor | 1
Part replacement on time | 1
Notes: Using the lettered categories mentioned earlier we divided the faults to get a better sense of what kind of MLC faults dominated the Indonesian data set. And though B faults were grater in number, they only made up a fraction of the downtime. Debilitating faults, type C faults, contributed to 95% of the total downtime. Compare this to machines in Oxford, where an MLC was down for longer than an hour only 23 times.

## Slide 27: Wider MLC Leaves
Can thicker leaves be more reliable?
Changing MLC no. of leaves/wider leaves:
  Minimal disruption to workflow
  Prevailing issues are Mechanical and need Replacement
Notes: Our second idea was to use wider and fewer leaves. This alternative will likely cause the least amount of disruption to workflow. Since mechanical faults is the prevailing issue and leaf motors needing to be replaced accounts for a majority of the replacement resolutions, having fewer leaves could be the ideal answer to this issue.

## Slide 28: Wider MLC Leaves
Can thicker leaves be more reliable?
Changing MLC no. of leaves/wider leaves:
  Minimal disruption to workflow
  Prevailing issues are Mechanical and need Replacement
Preliminary data shows that wider leaves might reduce data
  Decrease number of leaf motors
  Decrease the total contact surface area
Height, FJ, Kron, T, Willis, D, Chua, BH (2012) Impact of MLC leaf width on the quality of the dose distribution in partial breast irradiation., 37(1), 37-41. doi:10.1016/j.meddos.2010.12.011
Notes: Looking through the Indonesian data we can split the hospitals by how wide the MLC leaves are and then take an average of the percentage the MLC faults contribute to LINAC faults overall. Here we see a slight trend towards wider leaves causing fewer breakdowns, but the error bars are quite large. The thinking behind having wider leaves is that the machine would need few leaves, hence fewer motors, fewer moving parts and also decrease the total contact surface area between the leaves.

## Slide 29: Wider MLC Leaves
Can thicker leaves be more reliable?
Changing MLC no. of leaves/wider leaves:
  Minimal disruption to workflow
  Prevailing issues are Mechanical and need Replacement
Preliminary data shows that wider leaves might reduce data
  Decrease number of leaf motors
  Decrease the total contact surface area
How does this affect treatment quality?
Does changing the leaf width hinder patient care?
Height, FJ, Kron, T, Willis, D, Chua, BH (2012) Impact of MLC leaf width on the quality of the dose distribution in partial breast irradiation., 37(1), 37-41. doi:10.1016/j.meddos.2010.12.011
Notes: However, the next important question is how does this affect treatment quality? In the aim to achieve a more robust machine, we still have to avoid delivering a poorer level of treatment. As you can see in the figure, wider leaves leave a larger area for x-rays to pass through and potentially damage healthy cells. The parameter used to determine how closely a dose conforms to a tumor volume is called… the conformity index. Another parameter used is simply called OAR sparing and determines how much dose is delivered to Organs At Risk.

## Slide 30: Wider MLC Leaves
Study Design
Anonymised Patients provided by PMCC:
  12 Prostate
  10 Lung
  10 Colorectal
  10 Cervical
Compared leaf widths from different MLCs:
  2.5mm- 120HD
  5mm- Millennium 120
  10mm- Millennium 120
Plan Evaluation:
  Target Coverage & Dose Homogeneity
  Plan Robustness

## Slide 31: Wider MLC Leaves
Dose Metrics to the Target
The amount of coverage does increase with volume
Coverage from 10mm is on average better

## Slide 32: Wider MLC Leaves
Dose Metrics to the Target
The amount of coverage does increase with volume
Coverage from 10mm is on average better
Dose Homogeneity is relatively consistent
60

## Slide 33: Wider MLC Leaves
Plan Robustness Metrics
Monitor Units calculate machine usage
Monitor Units is not significantly different between leaf widths
Average Leaf Pair Opening (ALPO) is smaller for 10mm leaves
  Increased usage
  Fewer leaves

## Slide 34: Conclusions
Low and Middle Income Countries need reliable Radiotherapy
Multi-leaf Collimators require re-evaluation to make them more robust
MLC with wider leaves perform with the same quality as thinner leaves
  Especially 5mm and 2.5mm
Need more data to correlate leaf width and breakdown frequency
  More robustness data such as leaf acceleration
Notes: To conclude, though we have motivated the need for improved cancer care in LMICs, more breakdown data from countries of all income statuses are needed to properly correlate leaf size and breakdown frequency.
Other avenues for analysis include exploring other design parameters of the MLC such as the metal its made from and even looking to recent innovations like the SPHINX collimator and characterising the dosimetry in that.
These results will motivate the need and highlight the benefits of more reliable MLCs with fewer leaves to address the dramatic shortfall of Radiotherapy LINAC access in LMICs. And time really is of the essence here, because the longer we wait, the dramatic shortfall begins to steepen, and the burden becomes greater. But hopefully with this research and the work of many other brilliant minds, no matter where you’re from in the world, your cancer treatment will be Great and it will be Equal.

## Slide 35
Notes: To conclude, though we have motivated the need for improved cancer care in LMICs, more breakdown data from countries of all income statuses are needed to properly correlate leaf size and breakdown frequency.
Other avenues for analysis include exploring other design parameters of the MLC such as the metal its made from and even looking to recent innovations like the SPHINX collimator and characterising the dosimetry in that.
These results will motivate the need and highlight the benefits of more reliable MLCs with fewer leaves to address the dramatic shortfall of Radiotherapy LINAC access in LMICs. And time really is of the essence here, because the longer we wait, the dramatic shortfall begins to steepen, and the burden becomes greater. But hopefully with this research and the work of many other brilliant minds, no matter where you’re from in the world, your cancer treatment will be Great and it will be Equal.

## Slide 36: References
D. PISTENMAA AND N. COLEMAN (2017). Developing medical linacs for challenging regions. CERN Courier
O. BALOGUN, D. RODIN, W. NGWA (2016). Challenges and prospects for providing radiation oncology services in africa. Seminars in Radiation Oncology
L. M. WROE, T. A. IGE, O. C. ASOGWA (2019). Comparative analysis of radiotherapy LINAC downtime and failure modes in the UK, Nigeria and Botswana
R. ANDERSON, M. LAMEY, M. MACPHERSON (2015). Simulation of a medical linear accelerator for teaching purposes. Journal of Applied Clinical Medical Physics
W. M. DAVIS (2016). Dosimetric tranferability of a medical linear accelerator mounted mini-beam collimator
M. R. KARZMARK, C (1985). A Primer on Theory and Operation of Linear Accelerators in Radiation Therapy. US Bureau of Radiological Health
M. OLIVER, I. GAGNE, K BUSH (2010). Clinical significance of multi-leaf collimator positional errors for volumetric modulated arc therapy . Radiotherapy and Oncology
E. WILSON (2010). An Introduction to Particle Accelerators. Oxford
M. DOSANJH, A. AGGARWAL (2019). Developing Innovative, Robust and Affordable Medical Linear Accelerators for Challenging Environments
T. SHIMOZATO AND Y. AOYAMA (2017). Direct measurement of medical linear accelerator electron beam width at scattering foil position. International Journal of Medical Physics, Clinical Engineering and Radiation Oncology
E. STERPIN, Y. CHEN, W. LU (2011). On the relationships between electron spot size, focal spot size, and virtual source position in Monte Carlo simulations. Medical Physics
B. NORDELL AND A. BRAHME (1984). Angular distribution and yield from bremsstrahlung targets (for radiation therapy). Physics in Medicine and Biology

## Slide 37
Gregory Peiris
  gpeiris@student.unimelb.edu.au
Identifier first line
  Second line

## Slide 38
Back Up Slides
Greg Peiris
gpeiris@student.unimelb.edu.au
  13th Apr 2023
Notes: For the next few moments I will illustrate the need for reliable and affordable cancer care throughout the world, but especially in LMICs
And then outline the ways we plan to combat this issue as physicists

## Slide 39: Wider Leaves
What does the literature say?
How does this affect treatment quality?
Comparing several parameters across 17 papers and various anatomical sites
Majority of papers concluded that thinner leaves have better conformity and greater Organs At Risk sparing
Notes: From a literature search across 17 different papers comparing leaf widths to various treatment parameters across a wide range of anatomical sites, a majority of papers concluded that thinner leaves provide a higher quality of treatment. This includes better conformity index and delivering less dose to organs at risk among other factors.

## Slide 40: Wider Leaves
What does the literature say?
How does this affect treatment quality?
Comparing several parameters across 17 papers and various anatomical sites
Majority of papers concluded that thinner leaves have better conformity and greater Organs At Risk sparing
Notes: From a literature search across 17 different papers comparing leaf widths to various treatment parameters across a wide range of anatomical sites, a majority of papers concluded that thinner leaves provide a higher quality of treatment. This includes better conformity index and delivering less dose to organs at risk among other factors.
At this stage, it looks like we’re balancing a robust and reliable machine with one that can deliver high quality treatment. It’s not just the physics that needs to be changed and it’s not just a problem which needs re-engineering. Because by all accounts that can be done in a flash. We have to ensure that the clinical aspect is not being neglected in the process.
So, we spoke to some medical physicist and are now working along side a team radiologists and physicists at Peter MacCallum Cancer Centre to ensure all aspects are being appropriately accounted for.

## Slide 41: Wider Leaves
What does the literature say?
How does this affect treatment quality?
Comparing several parameters across 17 papers and various anatomical sites
Majority of papers concluded that thinner leaves have better conformity and greater Organs At Risk sparing
However
As tumor sizes get larger, leaf width differences vanish
Through LMICs, tumours tend to be large:
  Delay between diagnosis and treatment
  Larger growing types of cancers
  Lack of surgical options
Notes: And with their help, we did find a silver lining. We learnt that the advantage you get from thinner leaves mostly applies to small tumors. Once they get past a certain volume, this advantage disappears. Depending on the treatment technique used, the leaf width might not even matter at all.
And fortunately… well actually very unfortunately, we know that a majority of the tumours through sub-Saharan Africa and other Low Income regions can grow quite large.
As I mentioned at the beginning, this is due to the long delay between diagnosis and treatment in conjunction with the predisposition to get cancers that can grow large before detected and minimal access to surgical options.
But before this is implemented or even proposed, there is much more research and further analysis that needs to be done.

## Slide 42: Electron Beam Manipulation
Can we manipulate it?
Using a quadrupole, the aspect ratio can be changed
Maximum aspect ratio of 1.55:1
Idea #1
Notes: The first idea was the determine if we could shape the electron beam before it hit the target, reducing the strain on the MLC. The first task was to see how malleable the beam was, by introducing a quadrupole. We measure the aspect ratio which is just the ratio between the semi-major axis and semi-minor axis of an ellipse. We found that we could get it to peak at around 1.55:1

## Slide 43: Electron Beam Manipulation
All aspect ratios tend towards 1:1
1.55:1 will decrease by ~7%
What about bremsstrahlung?
Can we manipulate it?
Using a quadrupole, the aspect ratio can be changed
Maximum aspect ratio of 1.55:1
Idea #1
Notes: The next was concern is bremsstrahlung. Even if the beam was in the exact shape of the tumor, the randomness in bremsstrahlung could undo all the shaping. We found that as the thickness of the tungsten target increased, the aspect ratios all tended towards one. For an aspect ratio of 1.55:1 that meant a reduction by about 7%

## Slide 44: Electron Beam Manipulation
All aspect ratios tend towards 1:1
1.55:1 will decrease by ~7%
What about bremsstrahlung?
Can we manipulate it?
Using a quadrupole, the aspect ratio can be changed
Maximum aspect ratio of 1.55:1
1.55:1 is not the extend of manipulation we wanted
Adding more components increases complexity
Conclusions
Idea #1
Notes: But even after all of this, we concluded that 1.55:1 is nowhere near the level of manipulation we wanted. Something of the order 10:1 would have been better. The other concern was that adding a quadrupole might increase the complexity of the machine, introducing additional pathways to failure. It ends up being another component engineers and radiologists need to know how to fix on top of an already cumbersome machine.

## Slide 45: Robust Radiotherapy for Low- and Middle- Income Countries
The failure rate in LMICs is far worse than in HIC
There is potential to improve machine reliability with wider MLC leaves and not lose treatment plan quality
Conclusions
G. S. Peiris, B. Whelan, S. L. Sheehy
There is a dramatic shortfall of radiotherapy linear accelerators (RT LINACs) in Low and Middle Income Countries. By 2030, 75% of cancer related deaths will be in these nations and the technology they currently possess cannot handle the demand.
Background
RT LINACs are broken down for 7 times longer in LMICs than in High Income Countries and the MLC is responsible for a significant portion of the breakdowns.
Failure Rates and Downtime
The MLC is an x-ray collimator that shapes the beam to the size and shape of the tumour using tungsten leaves. Though the leaves have become thinner over time, perhaps using wider leaves can make the machines more reliable without compromising treatment quality.
Multi-Leaf Collimator (MLC)
Treatment plans were generated for an LMIC caseload to compare MLCs of differing leaf widths. The metrics compared were target conformity and
Treatment Plan Quality
compared were target conformity and dose homogeneity. In all anatomical sites, narrower leaf widths would provide a marginal improvement in dose homogeneity and target coverage. However, all leaf widths provide clinically acceptable results.
Homogeneity Index
Conformity Index
RI – Reference Isodose
TV – Target Volume
DXX- Dose to XX of Volume
References
1 Zubizareta E, Fidarova E, Healy B, Rosenblatt E, Need for radiotherapy in low and middle income countries – the silent crisis continues. Clin Oncol, 2015;27:P107-P114. doi: 10.1016/j.clon.2014.10.006
2 Pistenmaa D, Coleman N, Developing Medical Linacs for Challenging Regions. CERN Courier;2017.
3 L. Wroe, T. Ige, O. Asogwa, S. Aruah, S. Grover, R. Makufa, M. Fitz-Gibbon, and S. Sheehy, “Comparative analysis of radiotherapy linear accelerator downtime and failure modes in the UK, Nigeria and Botswana,” Clinical Oncology, vol. 32, no. 4, pp. e111–e118, 2020.
4 Peiris, GS, Pawiro, SA, Kasim, MF, Sheehy, SL. Failure modes and downtime of radiotherapy LINACs and multileaf collimators in Indonesia. J Appl Clin Med Phys. 2022;e13756. https://doi.org/10.1002/acm2.13756
Notes: But even after all of this, we concluded that 1.55:1 is nowhere near the level of manipulation we wanted. Something of the order 10:1 would have been better. The other concern was that adding a quadrupole might increase the complexity of the machine, introducing additional pathways to failure. It ends up being another component engineers and radiologists need to know how to fix on top of an already cumbersome machine.