## Slide 1: Particle and Nuclear Physics at the MeV scale in Australia
Martin Sevior1), Lindsey Bignell2,3), Catalina Curceanu4), Jackson Dowie2), David Jamieson1), Tibor Kibédi2), Andrew Stuchbery2), Andrea Tham1), Martin White5)
1) School of Physics, University of Melbourne
2)Department of Nuclear Physics and Accelerator Applications, Australian National University
3)ARC Centre of excellence for Dark Matter Particle Physics
4) INFN- LNF (Frascati)
5) University of Adelaide
Full Details: Sevior et al. https://arxiv.org/abs/2302.13281

## Slide 2: New Physics in the MeV regime?
Theoretical studies and experimental anomalies motivate a high-precision Time Projection Chamber for the Pelletron 5 MV accelerator at unimelb
Also enables qualitatively new Nuclear Physics experiments not previous possible
Employs advanced detector technology developed for HEP
The key: high resolution studies of electron-positron pairs from p + ZX →Z+1Y + (e+e-) reactions:
To start: p + 7Li →8Be + (e+e-)
The Pelletron accelerator laboratory, University of Melbourne

## Slide 3: Dark Photons and Axion Like Particles
Dark Matter => New Physics
MeV-GeV thermal relic DM requires new, comparably light mediators to achieve required annihilation cross-section for Thermal freeze-out.
Chart: 
| Dark Matter | Ordinary Matter
Region 1 | 80 | 20
A’
(Tim Nelson, SLACMass, Feb 2020)
~18.5 MeV
A’
e+
e-
.q
.e
Can produce ~ 5 - 22 MeV ’s
QCD has a CP-violating angle similar to the CKM matrix
in the range: , Neutron dipole moment=>
Strong CP problem!
The axion , feebly couples to gluons, photons and fermions
SM
Axion Like Particles (ALPs) arise from additional global symmetries:
In principle ALPS have different coupling to gluons , photons and fermions
Nuclear decays can explore viable ALP parameter-space and are sensitive to multi-TeV Physics!

## Slide 4: Particle Physics Motivation - Experiment
Well motivated theories for the existence of feebly interacting fundamental boson at the MeV scale.
ATOMKI group have found evidence for this at ~17 MeV invariant mass, the “X17”

## Slide 5: X17
Initial anomaly: (2016)
Also: (2021)
Also: (2022)
Initial signature: Unexpected larger yield of events at large opening angles
Better Signature: Invariant mass of = Mass of X17
~18.5 MeV
17 MeV (X17)
An opportunity to do fundamental Physics research on the Pelletron

## Slide 6: X17 particle
2016 observation1 p + 7Li→8Be + e+e-
20212: p + 3H→4He + e+e- 20223: p + 11B→12C + e+e-
proton beam
Nuclear target
e+e- pairs
detectors
1: arxiv 1504.01527,(PRL 116, 04215, (2016))


## Slide 7: X17 particle
2016 observation1 p + 7Li→8Be + e+e-
20212: p + 3H→4He + e+e- 20223: p + 11B→12C + e+e-
proton beam
Nuclear target
e+e- pairs
detectors
1: arxiv 1504.01527, ,(PRL 116, 04215, (2016)) 2: arxiv 2104.10075, (PRC 104,044003, (2021))


## Slide 8: X17 particle
2016 observation1 p + 7Li→8Be + e+e-
20212: p + 3H→4He + e+e- 20223: p + 11B→12C + e+e-
proton beam
Nuclear target
e+e- pairs
detectors
1: arxiv 1504.01527, ,(PRL 116, 04215, (2016)) 2: arxiv 2104.10075, (PRC 104,044003, (2021)) 3: arxiv 2209.10795, (PRC In Press)


## Slide 9: New Physics may exist at MeV- scale Observable via “” using Melbourne Pelletron
We plan to build a Time Projection Chamber (TPC) and perform far higher precision experiments on the Pelletron
ATOMKI X17 result
For p + 7Li→8Be + e+e-
X17
Our expectation from TPC
If the X17 exists
Invariant Mass
Invariant Mass
ATOMKI Energy Sum resolution ~1.5 MeV
TPC Energy Sum resolution 0.1 MeV

## Slide 10: Applications in Nuclear Physics
World-first double-differential IPC cross-section measurements
proton beam
Nuclear target
e+e- pairs
1Waltz et al. Nature,526:406 (2015)
Unobserved 2-quantum nuclear processes1:
double internal pair conversion
Both are qualitatively new Nuclear Physics investigations
Also, large acceptance enables investigation of multi-particle final states

## Slide 11: Time Projection Chamber to be installed on Pelletron
Iron Yoke (Electromagnet)
Trigger scintillators
Beam Pipe
Electric Field Cage
Proton beam

## Slide 12: TPC side view
Micromegas wire mesh
0V
15 KV
+800 V
Magnetic Field
Magnetic Field
Electric Field
Electric Field
Readout strips on PCB
+800 V
0 V
PCB
120 μm
Proton Beam
Scintillators
e-
e+
z = v×t
Ionization electrons
Drift with velocity v
Record (x,y,t)
Ionization electron

## Slide 13: Design of TPC
Conceptual design using EVE package in ROOT
Simulate electric fields inside the TPC and micromegas with COMSOL
Simulate Gas based detectors with HEP software GARFIELD
Simulate passage of primary electrons through TPC with Geant4
Record space-point hits with the expected resolution
Employ Genfit2 to reconstruct Particle trajectories
Employ RAVE to reconstruct interaction
Employ ROOT EVE for event display and visually validate reconstruction
Employ ROOT roofit to determine signal in the presence of background

## Slide 14: COMSOL electric field simulation of Field Cage
2D geometry with axial symmetry
Employed in COMSOL
3D geometry

## Slide 15: Projected x-y resolution ~ 100 microns
Design will work to provide 100 micron spatial resolution in (x,y)

## Slide 16: Geant 4 Simulations + Genfit2 + RAVE reconstruction
Developed reconstruction software using “genfit2” HEP software library to reconstruct tracks
Developed vertex reconstruction software using “RAVE” HEP software library to project tracks to a common vertex
Full Geant 4 simulation of the TPC

## Slide 17: Geant4 + Genfit2 + RAVE
Made numerous simulations. Include 100 µm resolution in x-y, 1 mm in z
Found detector gas 90:10 He / CO2 + thin Target chamber walls enable very good invariant mass resolution
Thin-walled Target Chamber is key
1 mm
Carbon
(ATOMKI)
50 µm
Mylar
 = 0.1 MeV
 = 0.37 MeV

## Slide 18: Prototype TPC Target Chamber
Shear strength of Mylar foil (15 kg/mm2) implies 50 micron thick foil has a factor of 20 safety under vacuum
Best Invariant Mass Resolution requires very thin vacuum wall

## Slide 19: Internal Conversion Background (IPC)
Peaks at low invariant mass
Simulated with Born-approximation
Full GEANT4 Simulation + genfit2 + RAVE reconstruction with realistic TPC hits (~130 )
Irreducible background comes from Nuclear Internal Conversion
Black line is an ansatz fit

## Slide 20: X17 + IPC background
Full simulation and reconstruction of IPC+X17 with 50 µm Mylar vacuum wall
4 Day run on Pelletron. 1µA proton beam, 1019 /cm2 7Li target
Quantify sensitivity as a function of BR relative to
ATOMKI found X17 with BR ~ at 6 σ
X17 BR=
1908 +- 45 events
42 σ significance

## Slide 21: 30 Day, , Populates state in 8Be*
90% Upper limits on BR()
Limits on ALP
Parameter space for ALP mass =17 MeV
Limits on ALP
Coupling as a function of ALP mass

## Slide 22: X17 + IPC background,
Target Thickness = Atoms/, proton beam, 30 Day Run
“X” boson produced at a rate 200 times less than X17

## Slide 23
No X17 signal => Next run at 4.5 MeV, Beam , Target , 30 - day run =>’s
(NA48 had data sample) Bump-hunt in Invariant-mass spectrum
World-best exclusion for prompt, weakly coupled bosons in 5 - 22 MeV range
90% Upper limits on BR()
IPC Background peaks at 1.1 MeV
Choose reaction for optimized X mass range
NA48 - Huge background at 5- 22 MeV
17.2
19.8
11.6
5.2
1.9

## Slide 24
Conclusions
Proposed TPC facility can exclude the X17 with > 2 orders of magnitude in an identical nuclear system
Unique facility – world-leading probe of dark photon/ALP physics. Others?
Significant first measurements for fundamental Nuclear Physics

## Slide 25: Backup

## Slide 26: Particle Physics Motivation – “Dark Sector”
Dark Matter => New Physics
MeV-GeV thermal relic DM requires new, comparably light mediators to achieve required annihilation cross-section for Thermal freeze-out.
Chart: 
| Dark Matter | Ordinary Matter
Region 1 | 80 | 20
A’
(Tim Nelson, SLACMass, Feb 2020)
~18.5 MeV
A’
e+
e-
.q
.e
Lee & Weinberg 77
Can produce ~ 5 - 22 MeV ’s

## Slide 27: Axion Like Particles (ALPs)
QCD has a CP-violating angle similar to the CKM matrix
in the range:
Neutron dipole moment=>
Strong CP problem!
Solved with the Peccei-Quinn symmetry
Broken by the vev of a SM singlet scalar field:
Scale of this field >> 1 TeV (given by )
The field acts as a space-time dependent field to cancel
Gives rise to a pseudo Nambu-Goldstone boson: axion
The axion , feebly couples to gluons, photons and fermions
SM
[Powell 16, Ringwald 16,Peccei&Quinn77;Weinberg 78; Wiczek 78]
Axion Like Particles (ALPs) arise from additional global symmetries:
Global lepton number symmetry: Majoron
[Chikashige et al. 78; Gelmini &Roncadelli 81]
Global family symmetry: Familon
[Wiczek 82; Berezhiani & Kholpov 90]
Quantum Gravity
[Bauer, Neubert, Renner, Schnubel, Thamm 22]
Then the particle corresponding to the excitation:
Is the axion
Excitations of the field orthogonal to this are called
Axion-Like-Particles (ALPs)
In principle ALPS have different coupling to gluons , photons and fermions
Nuclear decays can explore viable ALP parameter-space and hence are sensitive to multi-TeV Physics!

## Slide 28
ALP mass to gamma-coupling parameter-space

## Slide 29: Garfield simulation of drift velocity
Dispersion of drift velocity is ~ 0.6%
Gives rise to a z-resolution of ~ 1mm

## Slide 30: COMSOL electric field simulation of Field Cage
Default Electric field
radial Component
Default Electric field
Z Component
Optimized Electric field
radial Component
Default: 9 mm rings placed 1 mm apart
Optimized: 4.5 mm rings placed 0.5 mm apart
Initial upstream ring 1 mm downstream of cathode disk

## Slide 31: COMSOL + Garfield simulation of micromegas
+800 V
0 V
PCB
120 μm
Electrons are directed through the mesh and enter the amplification region

## Slide 32: Garfield simulation of Micromegas amplification
Electron avalanche providing gas gain
800 V over ~ 100 microns provides ~ 104 gas gain
Induces pulses of around 5 pC on readout strips
mesh

## Slide 33: LHC VMM ASICs + Scalable Readout System
Readout strips with VMM ASICs
~pC pulses from strips in the right range for VMM linear response
Records channel number, analogue charge, Time with 1 ns resolution and 64 µ-sec dynamic range
Programmable gain
Test charge input

## Slide 34: Geant 4 Simulations
As charged particles propagate through matter interact causing:
  “Multiple” small angle scattering causing direction change
  Energy loss as they transfer energy to the medium
  Ionization liberating electrons
Have set up a Geant 4 simulation of the TPC
Initial direction
Final direction
Accurate determination of the Invariant mass of the e+ e- pair requires a precise measurement of the magnitude and direction of the charged particles
Accurate simulation of multiple scattering required.
Minimize the effect.
Low Density, Low Z material

## Slide 35: Target Chamber
Prototype Target Chamber
Mylar foil on stainless steel pipe, nicely holds vacuum.
Reached 1.1×10-5 Torr (limited by outgassing in the connector)

## Slide 36: Garfield Simulation of electron release and drift
Around 100 electrons per track released via ionization.
Uncorrected Resolution
Corrected Resolution
Correlation in
Radial position
Corrected
10 μm resolution
100 μm resolution
Primary MeV-scale at z=0
Ionization electrons drift to detector at z=19 cm

## Slide 37: External Gamma conversion
Large flux of 18 MeV ’s from
These can externally convert via in material
Simulated of these
Low mass near the target limits conversions to 0.01%
Vertex constraint removes > 99%
Background is negligible compared to IPC

## Slide 38: Data rates
Comes from Thick-target bump hunt search + exclusion
Run at 4.5 MeV, Beam , Target
Cross Section for = 30 µb
N()/sec =
Approx 0.01% gamma’s convert = 7.5 events/sec
IPC rate = events/sec
12 Kbytes/event megabytes/sec
145 GB/day
4.5 TB for 30-day run
Well within the capacities of the unimelb Spartan HPC

## Slide 39: Comparison to LHCb for generic dark photon
TPC

## Slide 40: Search for the X17 at University of Montreal
Openning angle measurement of pairs from
arXiv:2211.11900v1