## Slide 1: Present Status of Siam Photon Source & Soft X-ray Beamline
Pat Photongkam
Beamline Scientist (BL3.2Ub) & Acting Chief of Beamline Design and Support Division
Research Facility Division
Synchrotron Light Research Institute
pat@slri.or.th

## Slide 2: About us
Synchrotron Light Research Institute
Nakhon-Ratchasima
Bangkok
Thailand synchrotron research center under supervision of the Ministry of Science and Technology.
Located in the area of Suranaree University of Technology, approx. 265 km from Suvarnabhumi international airport

## Slide 3: About us
Be a national research center with high efficiency in performing and promoting synchrotron research and development for sustainable development of Thailand
Local
SRA
SATI
Workshops
Training
South East Asia
SR2A
ASEAN Synchrotron Science Camp
ASEAN Workshop
International
Spring-8
NSRRC
CERN
DESY
ESRF
Daresbury Laboratory
Diamond
Australian Synchrotron
etc.
Vision
Target Groups
International Help & Support

## Slide 5: Siam Photon Source
Present Status (May 2018)
Storage ring
Decay mode
Electron energy = 1.2 GeV
Imax = 150 mA
Emittance = 61 nm.rad
Beamlines and End stations
10 beamlines with total of 12 end stations

## Slide 6: Siam Photon Source
Beam Service and Machine Shutdown
Round-1
Round-2
Shutdown
JAN - MAY
JUN - AUG
SEP - DEC
Holiday
Holiday
8.00 am – 9:00 am
8.00 am – 9:00 am
11 hrs / shift
Beam Injection

## Slide 7: Siam Photon Source
Number of annual Siam Photon Source users and publication during 2003-2017

## Slide 8: Siam Photon Source
Frequency of utilization on different classes of materials in published research during 2015-2017.

## Slide 9: Siam Photon Source
1.2 GeV Storage Ring
81.3m Circumference
24 BPM
1.2 GeV
Booster
Synchrotron
40 MeV Linac
6.5T SWLS
NSRRC
2.4T Hybrid MPW
ASTeC, Daresbury
Planar U60 PMM
Danfysik Co., Ltd
New SMPW
August 2018

## Slide 10: Development of Siam Photon Source
New 3 GeV Light Source
1996
1998
2001
2002
2003
2005
2009
2012
2014
2015
2016
2018
2019
2010
2011
2008
NSRC Project Approved
Installation, major parts from SORTEC
1.0 GeV storage ring, the first SR light
Install the 1st beamline: photoemission
Open service
1.2 GeV STR upgrade
XAS (BL8) & DXL
U60 Installation
TRXAS
PES, PEEM, SAXS & µ-XRF
XAS (BL5.2)
Fault Tolerant Control
MPW 2.4T & SWLS 6.5T
MXT, XMCT & IR
1.2 GeV Booster upgrade
Full Energy Injection
& SMPW
MX
BL ASEAN
RF Cavity upgrade
NSRC to SLRI

## Slide 11: Full Energy Injection
Problem of 1.0 to 1.2 GeV Ramp Up
High Load on machine components
Beam instability
Beam dump required for filling electron
More difficult for increasing # machine component
High level of adjustment required
2018
2016
2015
2014
2010
2005
2001
1.0 GeV
1 GeV Booster
1.2 GeV STR
U60 undulator
2.4T MPW
6.5T SWLS
1.2 GeV booster
RF cavity upgraded
Full Energy Injection
Benefit of Full Energy Injection
Filling electron without dumping beam
Requiring short time to stabilize
Low level of adjustment

## Slide 12: ASEAN Beamline
Photon Energy:
4-30 keV
Spot size ~ 20 micron
Proposed technique:
Micro XAS
Micro XRF & Imaging
2020
2019
2018
2017
2016
SMPW Design and Produce at NSRRC
New Bending Magnet Installed
Installation
SMPW & Beamline
End Station Installation & Commission
Officially Open
BL6b shutting down in May 2019

## Slide 13: Study New Electron Reference Orbit
Setting Reference Orbit
Reduce coupling
Reduce vertical beam size
Change vertical orbit in sextupole
Change the horizontal orbit in MPW
Increase Brightness
Reduce beam lifetime
Location | Upstream BPM | Downstream BPM
MPW | BPM1 | BPM2
BL1 | BPM3 | BPM4
BL2 | BPM6 | BPM7
U60 | BPM7 | BPM8
BL3 | BPM8 | BPM9
BL4 | BPM11 | BPM12
BL5 | BPM13 | BPM14
BL6 | BPM16 | BPM17
SWLS | BPM18 | BPM19
BL7 | BPM20 | BPM21
BL8 | BPM23 | BPM24

## Slide 14: Study New Electron Reference Orbit
BPM no. | Hor. Diff (mm) | Ver. Diff (mm)
BPM1 | 2.7115 | 0.2588
BPM2 | 2.6804 | 0.1246
BPM3 | 2.7382 | -0.0960
BPM4 | -0.1204 | -0.1569
BPM5 | 0.0499 | -1.1389
BPM6 | 0.0249 | -0.4248
BPM7 | 0.0063 | -0.0006
BPM8 | 0.0065 | 0.0001
BPM8 | -0.0484 | 0.1921
BPM10 | 0.3491 | -0.3057
BPM11 | 0.1296 | 0.2540
BPM12 | 0.1106 | 0.2190
BPM13 | 0.0533 | -0.1680
BPM14 | 0.1070 | 0.3139
BPM15 | 0.3735 | 0.5970
BPM16 | 0.0091 | 0.3383
BPM17 | 0.0918 | -0.0562
BPM18 | -0.8000 | 0.2109
BPM19 | -0.7726 | 0.2118
BPM20 | 0.1151 | 0.1191
BPM21 | 0.1607 | -0.8943
BPM22 | -0.0758 | -2.6322
BPM23 | -0.0793 | -1.1740
BPM24 | 2.7756 | 0.1678
Vertical direction
Horizontal direction

## Slide 15: Study New Electron Reference Orbit
Old Reference Orbit
New Reference Orbit
Optimize orbit in sextupole magnet
Bump orbit in MPW
Coupling 5.5%
Beam product 69,000 mA.min
Coupling 11.7%
Beam product 90,000 mA.min
Vertical beam size reduce by 30%

## Slide 16: Soft X-ray Beamline
Technical specification
Photon energy: 40-160, 220-1040 eV
Energy resolution: 1x10-4
Flux: 1x1010 phs/s
Beam size: < 1 mm2
2017
2013
2011
2010
2005
2001
1.0 GeV Bending Magnet
1.2 GeV STR upgrade
U60 undulator
BL3.2Ua: PES
BL3.2Ub: PEEM
New post-focusing mirror for BL3.2Ua
Harmonic Rejection for BL3.2Ua

## Slide 17: Soft X-ray Beamline
Three-bounce Harmonic Rejection Mirrors Chamber

## Slide 18: BL3.2Ua:PES
a) XPS Station
Technique: XPS, EY-XAS, FY-XAS
CLAM2 hemispherical analyzer (Thermo VG Scientific/VG Microtech)
SSD/MCP
Pico-ammeters
Current linear amplifier
Ion sputtering gun

## Slide 19: BL3.2Ua:PES
b) ARPES Station
Technique: ARPES
VG Scienta R4000 hemispherical analyzer (replaced Thermo VF Scientific ARUPS10 in 2014)
20K 6-axis sample manipulator
Ion sputtering gun
Sample heating capability
Sample Holder
SHOM type

## Slide 20: BL3.2Ua:PES
Currently not Available

## Slide 21
SERS chips (Ag NRs)
H gas sensor (Pt/WOx)
White LED (ZnONx)
http://dx.doi.org/10.1039/C6RA09972F
http://dx.doi.org/10.1021/am505127g
Metal oxide thin films, Nano-rods by OAD, Gas-timing dopes, SERS

## Slide 22
ACS Appl. Mater. Interfaces, 2017, 9 (17), pp 15192–15201.
Dr. Thomas
(NUS)
Dr. K. L. Woon
(UM)
J. Phys. D: Appl. Phys. 47 055109 (2014).
Dr. S. M. Hafiz (UPM)

## Slide 23
N K-edges
MCP with CsI: CF4655S144
Total fluorescence yield detector - first results on bulk-sensitive & non-conductive samples

## Slide 24
Norarat, R., Jainontee, K., Thianthaisong, W., Sriwang, S., Nakajima, H., Chienthavorn, O., ... & Whitlow, H. J. (2017).
MeV ion exposure behaviour of PMMA resist polymer studied by synchrotron light spectroscopies.
Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms, 404, 238-242.

## Slide 25: BL3.2Ub:PEEM
ELMITEC SPELEEM
Technique: PEEM, LEEM
Ion sputtering gun
0-100amu quadrupole mass spectrometers
PED / µ-ARPES
µ-XPS
X-PEEM, EF-PEEM
Locatelli, A., & Menteş, T. O. (2015). Chemical and Magnetic Imaging with X-Ray Photoemission Electron Microscopy. In Synchrotron Radiation (pp. 571-591). Springer, Berlin, Heidelberg.
Heatable Sample Holder
from RT to > 1400°C

## Slide 26
SLRI LEEM PEEM imaging analysis package
(made by Dr. Chanan Euaruksakul)

## Slide 27
Supruangnet, R., Morawe, C., Peffen, J. C., Nakajima, H., Rattanasuporn, S., Photongkam, P., ... & Busayaporn, W. (2016).
Chemical modification of B4C cap layers on Pd/B4C multilayers.
Applied Surface Science, 367, 347-353.

## Slide 28
Tunmee, S., Photongkam, P., Euaruksakul, C., Takamatsu, H., Zhou, X., Wongpanya, P., ... & Saitoh, H. (2016).
Investigation of pitting corrosion of diamond-like carbon films using synchrotron-based spectromicroscopy.
Journal of Applied Physics, 120(19), 195303.

## Slide 29
Kanjanachuchai, S., & Photongkam, P. (2017). Planar Self-Assembly of Submicron and Nanoscale Wires and Grooves on III–V (110) Surfaces.
Crystal Growth & Design, 17(8), 4413-4421.
Kanjanachuchai, S., & Euaruksakul, C. (2013). Directions and breakup of self-running in droplets on low-index InP surfaces.
Crystal Growth & Design, 14(2), 830-834.
InP(001)
InP(111)A
InP(111)B

## Slide 30
Mg map on AlSi3 alloy
Surface of AlSi based alloy at high temperature

## Slide 31
326C
342C
360C
370C
373C
379C
388C
402C
415C
Surface treatment for CuAgZr alloy

## Slide 32
Surface treatment for CuAgZr alloy
Ag 3d XPS intensity vs. annealing temperature
CuAgZr
Cold-rolled CuAgZr
(w/ a lot of dislocations)

## Slide 33
75 micron field of view
5 micron field of view
Graphene on SiC(0001)
1-layer
graphene
2-layer graphene
3-layer
graphene

## Slide 34
Polycrystalline surface of Fe 99.9% during 600C annealing
Pentacene Growth on Si wafer

## Slide 35
Fabrication of boron nitride flakes from iron alloy by annealing

## Slide 36: Beamline at SPS
BL1.1W: Multi X-ray Technique
XAS, XRF, WAXS and XRD
Contact: Dr Prae Chirawatkul (prae@slri.or.th)
BL1.2W: XTM
XMCT
Contact: Dr Catleya Rojviriya (catleya@slri.or.th)
BL1.3W: SAXS
SAXS and WAXS
Contact Dr Siriwat Soontaranon (siriwat@slri.or.th)
BL2.2: Multi X-ray Technique
Time resolved XAS
Contact Dr Yingyot Pooarporn (yingyot@slri.or.th)

## Slide 37: Beamline at SPS
BL3.2Ua: PES
XPS, USP, ARPES and soft-XAS
Contact: Dr Hideki Nakajima (hideki@slri.or.th)
BL3.2Ub: PEEM
PEEM, LEEM
Contact Dr Chanan Euaruksakun (chanan@slri.or.th)
BL4.1: IR Spectroscopy and Imaging
IR Spectromicroscopy
Contact Dr Kanjana Thamanu (kanjanat@slri.or.th)
BL5.2: XAS (SUT-NANOTEC-SLRI)
XAS and XRF
Contact Dr Pinit Kidkhunthod (pinit@slri.or.th)

## Slide 38: Beamline at SPS
BL6a: DXL
X-ray Lithography
Contact: Dr Rungruang Phatthanakun (rungruang@slri.or.th)
BL6b: XRF
micro-XRF and XRF imaging
Contact Dr Jitrin Chaiprapa (jitrin@slri.ro.th)
BL7.2W: MX
Macromolecule X-ray crystallography
Contact Dr Nuttawan Pramanpol (nuttawan@slri.or.th)
BL8: XAS
XAS and XRF
Contact Dr Wantana Klysubun (wantana@slri.or.th)

## Slide 39: BL1.1W: Multi X-ray Technique (MXT)
XRD setup is installing during shutdown 2018
Ionization chamber
Image plate detector
19 element Ge detector
Source | 2.4T Hybrid Magnet MPW
Monochromator type | DCM with Si(111)
Photon energy | 4 – 18keV
Energy resolution | 10-4
Photon flux | 107-1010 phs/s
Beam size (HxV) | 6 x 3 mm2
Technique | XAS, XRF, WAXS and XRD

## Slide 40: BL1.2W: X-ray Tomography Microscopy
Plan to install monochromator in 2019-2020
Source | 2.4T Hybrid Magnet MPW
Monochromator Type | Pink & Whitebeam
Photon Energy Range | 5 – 20keV
Photon flux | 4.6x1011 phs/s at 15keV
Beam size (HxV) | 10 × 4 mm2
Spatial Resolution | 1-5 micron

## Slide 41: BL1.3W: SAXS
Source | 2.4T Hybrid Magnet MPW
Monochromator type | DMM with W/B4C
Photon energy | 6 – 9keV
Energy resolution | 10-4
Photon flux | 3x109 phs/s
Beam size (HxV) | 2 x 1 mm2, 0.4 mrad divergence
Technique | SAXS and WAXS
Sample to detector | 4.5 m maximum (SAXS)
RAYONIX LX170HS
MARS SX165

## Slide 42: BL2.2: Time resolved XAS
Source | Bending magnet
Monochromator type | Energy dispersive bend crystal with Si (111) and Si(220)
Photon energy | 4.2 – 12 keV
Energy resolution | 10-3 - 10-2
Beam size (HxV) | 2 x 1 mm2
Technique | XAS (transmission)
Sample Environment | 0-600°C heating cell O2, N2, He, Ar and H2,

## Slide 43: BL4.1: IR Spectroscopy and Imaging
Source | Bending magnet
Photon energy | 0.01 - 0.5eV
Beam size (HxV) | 10 x 10 µm2
Technique | IR microspectroscopy
Spectrometer: | Vertex 70 spectrometer
Microscope: | Hyperion 2000 microscope
Detector | 250 micron MCT
Mode of measurement | Reflection, Transmission and Transfection

## Slide 44: BL5.2: XAS (SUT-NANOTEC-SLRI)
Only 1/3 of beamtime is managed by SLRI
Source | Bending magnet
Monochromator type | DCM with KTP(011), IsSb(111) Ge(220)
Photon energy | 1.24 – 12.1 keV
Energy resolution | 2x10-4
Beam size (HxV) | 13 x 1 mm2 (transmission) 20 x 1 mm2 (fluorescence)
Technique | XAS & XRF
Sample Environment | In-situ heating cell O2, N2, He, Ar and H2 max. flow rate 100 ml/min (N2)

## Slide 45: BL6a: DXL
Source | Bending magnet
Monochromator type | White beam
Beam size (HxV) | 6 × 2 mm2
Technique | X-ray Lithography
Good sensitivity
Exposed area absorb
developer (distortion)
Radiation (UV/X-ray)
Mask
Photosensitive materials
Substrate (e.g. Si, glass)
Photosensitive materials
Change only when exposed to radiation
Spray substrate with
developer solution
Positive resist, developer-
solution removes exposed area
b) Negative resist, developer-
solution removes unexposed area

## Slide 46: BL6a: DXL
Supporting Facilities
Class 100 clean room - e-beam lithography
Class 1,000 clean room - UV lithography
Class 10,000 clean room – thin film deposition
Flexible humidity sensor on PET substrate
Sensitivity of 0.027 pF/%RH
(wearable device and packaging)
Flexible microhotplate on PET substrate

## Slide 47: BL6b: µ-XRF
Source | Bending magnet
Monochromator type | White beam
Photon energy | 2 - 10 keV
Beam size (HxV) | 100 × 100 µm2
Technique | µ-XRF and Imaging
Detector | Si(PIN) detector with energy resolution of 160 eV

## Slide 48: BL7.2W:MX
Source | 6.4T SWLS
Monochromator type | DCM
Photon energy | 7-18 keV
Flux | 1 x 109 phs/s at 8keV
Beam size (HxV) | 2.5 × 1.5 mm2
Technique | MacromolecularX-ray Crystallography
Detector | marCCD SX165
Sample Environment | 100K with Oxford Cryosystems: 700 series cryostream nitrogen cooler
Supporting Facilities
Protien Crytalization Lab

## Slide 49: BL8: XAS
Source | Bending magnet
Monochromator type | DCM with KTP(011), IsSb(111), Si(111) and Ge(220)
Photon energy | 1.2 - 13 keV
Energy resolution | 1x10-4 to 3x10-4
Flux | 1x108 - 1x1010 phs/s/100mA
Beam size (HxV) | 13 × 2 mm2
Technique | XAS & XRF
Supporting Facilities
Ionization Chamber
Si drift detector (4 channel)
13 element Ge detector

## Slide 50: BL5.3: XPS (SUT-NANOTEC-SLRI)
PHI 5000 VersaProbe II Scanning XPS Microprobe
Contact: Dr Narong Chanlek (narong@slri.or.th)
The end station for coming up beamline

## Slide 51: Thailand 3.0 GeV Synchrotron Light Source
The project is during submission for drafting the 13th national economic and social development plan (2022-2026)
The detail design reports have deadline on Sep 2019
7 beamlines will be construct in the 1st phase

## Slide 52: Thailand 3.0 GeV Synchrotron Light Source
Storage Ring
Beam emittance < 1.0 nm•rad at beam current of 300 mA
Storage ring circumstance 321.3m by 14 cells of DTBA lattice
Beamline in 1st Phase
High Resolution Soft X-ray Spectroscopy
Tender X-ray absorption spectroscopy
Hard X-ray absorption spectroscopy
Small and Wide Angle X-ray scattering
High resolution X-ray diffraction
Macromolecular crystallography
X-ray microtomography
Nakhon-Ratchasima
Rayong
Candidate Location

## Slide 53
THANK YOU FOR YOUR ATTENTION