## Slide 1
Kevin Jordan
Beam Diagnostics Collaboration Meeting 3/18/15
MEIC Design Overview

## Slide 2
MEIC Design Goals
Energy
  Full coverage of √s from 15 to 65 GeV
  Electrons 3-10 GeV, protons 20-100 GeV, ions 12-40 GeV/u
Ion species
  Polarized light ions: p, d, 3He, and possibly Li
  Un-polarized light to heavy ions up to A above 200 (Au, Pb)
Space for at least 2 detectors
Full acceptance is critical for the primary detector
Luminosity
  1033 to 1034cm-2s-1 per IP in a broad CM energy range
Polarization
  At IP: longitudinal for both beams, transverse for ions only
  All polarizations >70%
Upgrade to higher energies and luminosity possible
  20 GeV electron, 250 GeV proton, and 100 GeV/u ion
  Design goals consistent with the White Paper requirements

## Slide 3: Design strategy: High Polarization
All rings are figure-8  critical advantages for both ion and electron beam
  Spin precessions in the left & right parts of the ring are exactly cancelled
  Net spin precession (spin tune) is zero, thus energy independent
  Spin is easily controlled and stabilized by small solenoids or other compact spin rotators
  Advantage 1: Ion spin preservation during acceleration
  Ensures spin preservation
  Avoids energy-dependent spin sensitivity for all species of ions
  Allows a high polarization for all light ion beams
  Advantage 2: Ease of spin manipulation
    Delivers desired polarization at the collision points
  Advantage 3: The only practical way to accommodate polarized deuterons
  (given the ultra small g-2)
  Advantage 4: Strong reduction of quantum depolarization thanks to the energy independent spin tune.

## Slide 4: Baseline Layout
Ion Source
Booster
Linac
Ion Source
Booster
Linac
MEIC Cost Review December 18 2014
CEBAF is a full energy injector.
Only minor gun modification is needed
Warm Electron
Collider Ring
(3 to 10 GeV)

## Slide 5: Campus Layout
~2.2 km circumference
E-ring from PEP-II
Ion-ring with super-ferric magnets
Tunnel consistent
with a 250+ GeV upgrade

## Slide 6: MEIC Baseline
Baseline for the cost estimate
Collider ring circumference: ~2200 m
Electron collider ring and transfer lines : PEP-II magnets, RF (476 MHz) and vacuum chambers
Ion collider ring: super-ferric magnets
Booster ring: super-ferric magnets
SRF ion linac
Energy range
Electron: 3 to 10 GeV
Proton: 20 to 100 GeV
Lead ions: up to 40 GeV
Design point | p energy (GeV) | e- energy (GeV) | Main luminosity limitation
low | 30 | 4 | space charge
medium | 100 | 5 | beam beam
high | 100 | 10 | synchrotron radiation

## Slide 7: MEIC Electron Complex
IP
Dx(m)
x(m), y(m)
Electron Collider Ring Optics
CEBAF provides up to 12 GeV, high repetition rate and high polarization (>85%) electron beams, no further upgrade needed beyond the 12 GeV CEBAF upgrade.
Electron collider ring design
  circumference of 2154.28 m = 2 x 754.84 m arcs + 2 x 322.3 m straights
  Meets design requirements
  Provides longitudinal electron polarization at IP(s)
  incorporates forward electron detection
  accommodates up to two detectors
  includes non-linear beam dynamics
  reuses PEP-II magnets, vacuum chambers and RF
Beam characteristics
  3A beam current at 6.95 GeV
  Normalized emittance 1093 mm @ 10 GeV
  Synchrotron radiation power density 10kW/m
  total power 10 MW @ 10 GeV
CEBAF and the electron collider provide
the required electron beams for the EIC.

## Slide 8: Electron Collider Ring Layout
  Circumference of 2154.28 m = 2 x 754.84 m arcs + 2 x 322.3 m straights
Figure-8, crossing angle 81.7
e-
R=155m
RF
RF
Spin rotator
Spin rotator
CCB
Arc, 261.7
81.7
Forward e- detection
IP
Tune trombone & Straight FODOs
Future 2nd IP
Spin rotator
Spin rotator
  Electron collider ring w/ major machine components

## Slide 9: Electron Ring Optics Parameters
Electron beam momentum | GeV/c | 10
Circumference | m | 2154.28
Arc net bend | deg | 261.7
Straights’ crossing angle | deg | 81.7
Arc/straight length | m | 754.84/322.3
Beta stars at IP *x,y | cm | 10/2
Detector space | m | -3 / 3.2
Maximum horizontal / vertical  functions x,y | m | 949/692
Maximum horizontal / vertical dispersion Dx,y | m | 1.9 / 0
Horizontal / vertical betatron tunes x,y |  | 45.(89) / 43.(61)
Horizontal / vertical chromaticitiesx,y |  | -149 / -123
Momentum compaction factor  |  | 2.2 10-3
Transition energy tr |  | 21.6
Horizontal / vertical normalized emittance x,y | µm rad | 1093 / 378
Maximum horizontal / vertical rms beam size x,y | mm | 7.3 / 2.1

## Slide 10: CEBAF - Full Energy Injector
CEBAF fixed target program
  5-pass recirculating SRF linac
  Exciting science program beyond 2025
  Can be operated concurrently with the MEIC
CEBAF will provide for MEIC
  Up to 12 GeV electron beam
  High repetition rate (up to 1497 MHz)
  High polarization (>85%)
  Good beam quality up to the mA level

## Slide 11: Ion Collider Ring
Figure-8 ring with a circumference of 2153.9 m
Two 261.7 arcs connected by two straights crossing at 81.7
R = 155.5 m
Arc, 261.7
IP
disp. supp./
geom. match #3
disp. supp./
geom. match #1
disp. supp./
geom. match #2
disp. supp./
geom. match #3
det. elem.
disp. supp.
norm.+
SRF
tune
tromb.+
match
beam exp./
match
elec. cool.
ions
81.7
future 2nd IP

## Slide 12: Ion Collider Ring Parameters
Circumference | m | 2153.89
Straights’ crossing angle | deg | 81.7
Horizontal / vertical beta functions at IP *x,y | cm | 10 / 2
Maximum horizontal / vertical beta functions x,y max | m | ~2500
Maximum horizontal dispersion Dx | m | 3.28
Horizontal / vertical betatron tunes x,y |  | 24(.38) / 24(.28)
Horizontal / vertical natural chromaticitiesx,y |  | -101 / -112
Momentum compaction factor  |  | 6.45  10-3
Transition energy tr |  | 12.46
Normalized horizontal / vertical emittance x,y | µm rad | 0.35 / 0.07
Horizontal / vertical rms beam size at IP *x,y | µm | ~20 / ~4
Maximum horizontal / vertical rms beam size x,y | mm | 2.8 / 1.3
All design goals achieved
Resulting collider ring parameters
Proton energy range | GeV | 20(8)-100
Polarization | % | > 70
Detector space | m | -4.6 / +7
Luminosity | cm-2s-1 | > 1033

## Slide 13: MEIC super-ferric dipole
2 X 4m long dipole
NbTi cable
3 T
Correction sextupole
Common cryostat
Collaboration with Peter McIntyre Texas A&M Univ.

## Slide 14: Ion Injector Complex - Overview
Ion Sources
SRF Linac (285 MeV)
Booster (8 GeV)
(accumulation)
DC e-cooling
Status of the ion injector complex:
Relies on demonstrated technology for injectors and sources
Design for an SRF linac exists
8 GeV Booster design to avoid transition for all ion species and based on
super-ferric magnet technology
Injection/extraction lines to/from Booster are designed

## Slide 15: Ion Linac - Parameters and Layout
Ion species: p to Pb | 
Ion species for the reference design | 208Pb
Kinetic energy (p, Pb) | 285 MeV 100 MeV/u
Maximum pulse current: Light ions (A/Q<3) Heavy ions (A/Q>3) | 2 mA 0.5 mA
Pulse repetition rate | up to 10 Hz
Pulse length: Light ions (A/Q<3) Heavy ions (A/Q>3) | 0.50 ms 0.25 ms
Maximum beam pulsed power | 680 kW
Fundamental frequency | 115 MHz
Total length | 121 m
Optimum stripping energy: 13 MeV/u
10 cryostats
4 cryostats
2
Ion Sources
QWR
QWR
HWR
IH
RFQ
MEBT
10 cryos
4 cryos
2 cryos
Linac design based on the ANL linac for FRIB
Pulsed linac capable of accelerating multiple
charge ion species (H- to Pb 67+)
Warm Linac Sections: (115 MHz)
RFQ (3m)
MEBT (3m)
IH structure (9m)
Cold linac sections:
QWR + QWR (24m + 12 m) 115 MHz
Stripper, chicane (10m) 115 MHz
HWR section (60m) 230 MHz

## Slide 16: Booster (8 GeV, gt = 10)
injection
extraction
RF cavity
Crossing angle:
75 deg.
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Straight
Inj. Arc (2550)
Straight (RF + extraction)
Arc (2550)
Injection: multi-turn 6D painting
  0.22-0.25 ms long pulses ~180 turns
  Proton single pulse charge stripping at 285 MeV
  Ion 28-pulse drag-and-cool stacking at ~100 MeV/u
  Ion energies scaled by mas-to-charge ratio to preserve magnetic rigidity
Ekin = 285 MeV – 8 GeV
Ring circumference: 273 m
(≈ 2200/8)

## Slide 17: MEIC Multi-Step Cooling Scheme
ion sources
ion linac
Booster
(0.285 to 8 GeV)
collider ring
(8 to 100 GeV)
BB cooler
DC cooler
Ring | Cooler | Function | Ion energy | Electron energy
 |  |  | GeV/u | MeV
Booster ring | DC | Injection/accumulation of positive ions | 0.11 ~ 0.19 (injection) | 0.062 ~ 0.1
 |  | Emittance reduction | 2 | 1.1
Collider ring | Bunched Beam Cooling (BBC) | Maintain emittance during stacking | 7.9 (injection) | 4.3
 |  | Maintain emittance | Up to 100 | Up to 55
DC cooling for emittance reduction
BBC cooling for emittance preservation

## Slide 18: MEIC Bunched Beam Electron Cooler
ion bunch
electron bunch
Cooling section
solenoid
SRF Linac
dump
injector
energy recovery
Baseline cooling requirements and solution
Emittance 0.5 to 1 mm mrad  reduced IBS effect
Magnetized beam, up to 55 MeV energy, and 200 mA current
Need linac for acceleration
Must utilize energy-recovery-linac (beam power is 11 MW)
Cooling by a bunched electron beam
Electron energy | MeV | up to 55
Current and bunch charge | A / nC | 0.2 / 0.42
Bunch repetition | MHz | 476
Cooling section length | m | 60
RMS Bunch length | cm | 3
Electron energy spread | 10-4 | 3
Cooling section solenoid field | T | 2
Beam radius in solenoid/cathode | mm | ~1 / 3
Solenoid field at cathode | KG | 2
Notes: 18

## Slide 19: Performance MEIC baseline
Achieved with a single pass ERL cooler
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | E | p | e
Beam energy | GeV | 30 | 4 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 159 | 
Particles per bunch | 1010 | 0.66 | 3.9 | 0.66 | 3.9 | 2.0 | 2.8
Beam current | A | 0.5 | 3 | 0.5 | 3 | 0.5 | 0.72
Polarization | % | >70% | >70% | >70% | >70% | >70% | >70%
Bunch length, RMS | cm | 2.5 | 1.2 | 1 | 1.2 | 2.5 | 1.2
Norm. emitt., vert./horz. | μm | 0.5/0.5 | 74/74 | 1/0.5 | 144/72 | 1.2/0.6 | 1152/576
Horizontal and vertical β* | cm | 3 | 5 | 2/4 | 2.6/1.3 | 5/2.5 | 2.4/1.2
Vert. beam-beam param. |  | 0.01 | 0.02 | 0.006 | 0.014 | 0.002 | 0.013
Laslett tune-shift |  | 0.054 | small | 0.01 | small | 0.01 | small
Detector space, up/down | m | 7/3.6 | 3.2 / 3 | 7/3.6 | 3.2 / 3 | 7/3.6 | 3.2 / 3 (3)
Hour-glass (HG) reduction |  | 0.89 |  | 0.88 |  | 0.73 | 
Lumi./IP, w/HG, 1033 | cm-2s1 | 1.9 |  | 4.6 |  | 1.0 | 
Horizontal and vertical β* | cm | 1.2 | 2 | 1.6 / 0.8 | 1.6 / 0.8 | 2 /1 | 1.6 / 0.8
Vert. beam-beam param. |  | 0.01 | 0.02 | 0.004 | 0.021 | 0.001 | 0.021
Detector space, up/down | m | ±4.5 | 3 | ±4.5 | 3 | ±4.5 | 3
Hour-glass (HG) reduction |  | 0.67 |  | 0.74 |  | 0.58 | 
Lumi./IP, w/HG, 1033 | cm-2s1 | 3.5 |  | 7.5 |  | 1.4 | 
For a full acceptance detector
For a high(er) luminosity detector

## Slide 20: Conclusions and Outlook
The MEIC baseline based on a ring-ring design is mature
and can deliver luminosity from a few 1033 to a few 1034
and polarization over 70% in the 15-65 GeV range with low
technical risks.
The MEIC baseline fulfills the requirements of the white paper.
We continue to optimize the present design for cost and performance.
The design is upgradeable in energy and luminosity.
Many thanks to Fulvia Pilat & Yuhong Zhang for the slides