## Slide 1: Fission Neutron Tomography of a 280-L Waste Package - A feasibility study
Dr. Thomas Bücherl
Technische Universität München
ZTWB Radiochemie München (RCM)
Sydney, September 5, 2018

## Slide 2: Content
Motivation
NECTAR
Test sample
Measurements
Transmission measurements
  Data evaluation
  Results
Emission measurements
  Data evaluation
  Results
Summary

## Slide 3: Motivation
Radioactive waste has many origins
nuclear power plants
nuclear medicine
research institutes
research reactors
accelerators
radionuclide sources
...
Radioactive material has isotope specific half-lives
  intermediate disposal: wait for free release or storage in ..
final disposal
 Non-destructive characterization of waste packages
Some of the waste packages to be characterized
Notes: Most of you are working with neutrons; Generation of Neutrons; Reactors; Accelerators; Radionuclide sources; etc.

## Slide 4: Motivation
At ITMNR-9 (Beijing, China) results of a feasibility study on reactor based fission neutron radiography of 200-l waste packages was presented [1].
 Extend study to fission neutron tomography
NECTAR
[1] T. Bücherl, O. Kalthoff, Ch. Lierse von Gostomski, A feasibility study on reactor based fission neutron radiography of 200-l waste packages, Physics Procedia (2017) pp. 64-72 DOI: 10.1016/j.phpro.2017.06.008.
fission neutrons
-radiography (60Co)

## Slide 5: Motivation
Radioactive waste may contain neutron emitters.
Estimation of detection limits for neutron sources located inside waste packages
Feasability study on neutron emission tomography
NECTAR
Photograph of a radionuclide based neutron source (AmBe)
200-l drum on the sample manipulator at NECTAR

## Slide 6: NECTAR
Fission neutron spectrum
Emean= 1.8 MeV
min = 8.7E+05 cm-2s-1
max = 4.7E+07 cm-2s-1
(L/D) ~ 135 up to 233
Sample space (max)
approx. 80 cm x 80 cm x 80 cm
approx. 800 kg
Detection system
different converters
CCD-camera (e.g. Andor iKon-L 936)
FOV  30 cm x 30 cm
NEW: Thermal spectrum available, too!
 Presentation of Samantha Zimnik

## Slide 7: Test sample
Preparation of the sample
insert pellets ….
… and some scrap in a 200-l drum

## Slide 8: Test sample
Preparation of the sample (cont.)
The equipped 200-l drum is then placed in a 280-l drum.
Data:
total weight: about 500 kg
diameter: 71.0 cm
height : 100.3 cm
280-l drum on the sample manipulator at NECTAR

## Slide 9: Measurements
Transmission measurements (TCT)
Object: 280-l drum
max. FOV: 291 mm x 288 mm (w x h)
scanning: 3 images/projection with distance of 230 mm each (70 mm, 300 mm, 530 mm)
scan-direction: forward-rotation-backward (minimization of measuring time)
measuring time: 60 s per position
measuring mode: golden ratio (in total 491 angular positions over 360°)

## Slide 10: Measurements
Emission measurements (ECT)
Objects:
AmBe-sources
  37 GBq (1 Ci) and 2.2·105 n/s
  370 GBq (10 Ci) and 2.2·106 n/s
  Measurements
  source(s) in PE-cylinder in drum
  source(s) in drum (outside PE cylinder)
  10 Ci source in front of detector
  Remark: Measurements performed with different converter screens (thermal and fast neutron types)
Photograph of a radionuclide based neutron source (AmBe)

## Slide 11: Data evaluation - transmission measurements
raw data
filtering [2]
normalization
  corrected for dark image and open beam image
  limit to interval [0;1]
  multiply data by a factor of 20000 to store as *.tif
cropping (150 pixels on all sides of)
tilt-correction
stitching
shift-correction
reconstruction (FBP)
[2] K. Osterloh, T. Bücherl, U. Zscherpel und U. Ewert, Image recovery by removing stochastic artefacts identified as local asymmetries, Journal of Instrumentation, 7(04):C04018, 2012, DOI: 10.1088/1748-0221/7/04/C0401

## Slide 12: Results – transmission measurements
Raw data after filtering
„Dynamic“ range: 1000 to 1660

## Slide 13: Results – Transmission measurements
Data ready for reconstruction
Some “interesting” observations:
Some “moving” objects
Stitching not really satisfying!

## Slide 14: Results – Transmission measurements
Stitching

## Slide 15: Results – Transmission measurements
Stitching
327.54°
Overlap of 143 pixels
327.54 °

## Slide 16: Results – Transmission measurements
Stitching
327.54°
Overlap of 143 pixels
52.52°
Overlap of 143 pixels

## Slide 17: Results – Transmission measurements
Stitching
52.52 °
Overlap of 189 pixels
52.52°
Overlap of 143 pixels

## Slide 18: Results – Transmission measurements
52.52 °
Overlap of 189 pixels
52.52°
Overlap of 143 pixels
Stitching process remains a big challange!
Difference of ~ 7 mm

## Slide 19: Results – Transmission measurements
Due to beam divergence, scattering effects etc. reconstruction does not result in an acceptable image quality

## Slide 20: Comparison with g-transmission measurements
Integrated Tomgraphy System (ITS) @ RCM
3D
2D
g-transmission tomography is still superior to fission neutron transmission tomography!

## Slide 21: Data evaluation - emission measurements
raw data (2048 pixels x 2048 pixels)
binning (5 pixels)
shift-correction
reconstruction with
  FBP and
  Maximum likelihood maximum estimator[3] (MLEM)
[3] http://campar.in.tum.de/twiki/pub/Main/MoritzBlume/EMPET.pdf

## Slide 22: Results – emission measurements
No images, when sources were in the drum (any position)
  Sources too weak!
  Rough estimation:
  minimum distance sample – converter: 30 cm
  no attenuation assumed
  source strength: 2.2∙106 s-1
   about 900 n/cm2
   about 0,2 n/pixel
   measuring time of much more than 1 hour per projection required!

## Slide 23: Results – emission measurements
  „Strong“ source close to the detector
    distance: 3 cm
    converter for fast neutrons
    measuring time per image: 3500 s per projection
    golden ratio (in total 207 angular positions)

## Slide 24: Results – emission measurements
„Dynamic“ range: 1662 to 1926

## Slide 25: Results – emission measurements
MLEM-reconstruction after 30 iterations and smoothing filter applied
FBP-reconstruction using ramp-filter

## Slide 26: Summary and Outlook
Is fission neutron tomography on large volume samples possible?
Yes, but …
  challenges arise from
    image processing (especially stitching) and
    “moving” objects
    Further investigations required  next R&D topics!
  applicability depends strongly on the matrix composition (material, density, thickness)
  neutron flux available at NECTAR is on the lower limit for these investigations

## Slide 27: Summary and Outlook
Is neutron emission tomography on large volume samples possible?
Yes, but …
  - it strongly depends on their neutron emission rates
 Emission neutron tomography at NECTAR was demonstrated, but is only applicable in praxis on large samples (like real waste packages) for extremely high neutron emission rates.
SANDRA
Special Arrangement for Neutron Detection in Radioactive Waste packages

## Slide 28: How to get beam time at NECTAR
get into contact with me (thomas.buecherl@tum.de)
discuss feasibility of planned measurement
submit a proposal (see http://mlz-garching.de/user-office)
if accepted, contact me for arranging beam time
NEW: Thermal neutrons available at NECTAR, too!

## Slide 29
Acknowledgment:
Dr. Christoph Lierse von Gostomski
Thomas Baldauf