## Slide 1: BEHAVIOR OF POROUS ROCK STUDIED WITH NEUTRON TOMOGRAPHY
Maddi Etxegarai
E. Tudisco, A. Tengattini, S. Hall, G. Viggiani

## Slide 2
Context
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
Changes in the fluid flow due to the deformations during subsurface resource engineering operations are of great interest yet poorly understood.
There is a clear need for experimental characterization and modelling of how deformation modifies fluid flow in rocks

## Slide 3
X-rays allow high spatial and temporal resolution.
BENTHEIM SAMPLE
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
Context: X-rays
Notes: But we want to analyze the hydrolical aspects

## Slide 4
Edward Andò
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
Context: Neutrons
Neutrons are highly sensitive to hydrogen.
Different interaction with each isotope.
Low interaction with metals.
Notes: Contrast , D2O, H2O
Cell

## Slide 5
Objective
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
Perform an experimental campaign to measure the full field fluid speed evolution in rocks at different triaxial loading stages.
High speed neutron tomographies are acquired in order to track the 3D fluid front.
Medium resolution x-ray tomographies have also been acquired to obtain the strain field by means of Digital Volume Correlation
→ AIM: TO QUANTIFY COUPLED HYDROMECHANICAL PROCESSES
Notes: What do we need to get that

## Slide 6
Objective: structure of the experimental campaign
A0 – SANDSTONE SAMPLE
A0
A1
A2
A3
Sandstone sample
A1 - X_RAY TOMOGRAPHY
3D reconstruction
X-Ray tomography
A2 - TRIAXIAL LOADING
Local discontinuities
Triaxial loading
A3 - X_RAY TOMOGRAPHY
3D reconstruction
X-Ray tomography
DIGITAL VOLUME CORRELATION
3D MAXIMUM SHEAR STRAIN FIELD
3D VOLUMETRIC STRAIN FIELD
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 7
Objective: structure of the experimental campaign
7
B1 – SATURATED SAMPLE
D2O
B0
Saturated sample
B1
Neutron high speed tomography
05 – NEUTRON HIGH SPEED TOMOGRAPHY
3D reconstructions
H2O
IN-HOUSE CODE
3D
SPEED MAP
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 8
Chart: VO05ME
Test: Triaxial loading
Chart: VO03ME
Confining pressure (Mpa)
Chart: VO02ME
Chart: VO04ME
Confinement pressure: 40 MPa
Confinement pressure: 30 MPa
4 Vosges samples were deformed at different levels + 1 intact
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 9
Test: Neutron setup
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
The samples were previously saturated with heavy water.
Light water was pushed through the sample while the flow rate and the pressure were controlled.

## Slide 10
Image analysis: Reconstruction
One minute fast tomography
                -Radiography exposure time: 0.2 s
                -Pixel size: 220 µm
Beam hardening effect
Not a strong contrast between the gray scale of both waters
H2O
D2O
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 11
Image analysis: Time map
0
412
min
SIGMOIDAL FITTING
The gray scale of a pixel is plotted for all the tomographies and a sigmoidal function is fitted to the trend
The C parameter gives the arrival time
WATER FRONT TIME MAP
C
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 12
Image analysis: Water front speed
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY
Binarize the reconstructed volume to get the two consecutive fronts.
Calculate the distance maps in the space between both fronts.
Sum both distance maps

## Slide 13
Results: VO01ME
Attenuation
X-RAY TOMOGRAPHY
Intact sample
The water was flushed at 4 ml/h: Front speed of 0.253 mm/min
Vertical
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 14
Results: VO01ME
0
mm/min
0.34
WATER FRONT SPEED
X-RAY TOMOGRAPHY
Intact sample
The water was flushed at 4 ml/h: Front speed of 0.253 mm/min
Attenuation
Vertical
Vertical
Horizontal
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 15
Results: VO02ME
0.01
0.22
-0.1
0.1
Sample deformed at 30 MPa confinement, in the beginning of the plateau in the stress/strain response
The water was flushed 8 ml/h:
Front speed of 0.506 mm/min
SHEAR STRAIN
VOLUMETRIC STRAIN
Vertical
Vertical
Horizontal
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 16
Results: VO02ME
0.04
mm/min
0.59
SHEAR STRAIN
VOLUMETRIC STRAIN
0.01
0.22
-0.1
0.1
Sample deformed at 30 MPa confinement, in the beginning of the plateau in the stress/strain response
The water was flushed 8 ml/h:
Front speed of 0.506 mm/min
WATER FRONT SPEED
Vertical
Vertical
Horizontal
Horizontal
Vertical
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 17
Results:VO03ME
0.006
-0.015
0.015
0.02
Sample deformed at 30 MPa confinement, close to the stress peak
The water was flushed at 4 ml/h
Front speed of 0.253 mm/min
SHEAR STRAIN
VOLUMETRIC STRAIN
Vertical
Vertical
Horizontal
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 18
Results:VO03ME
0.19
mm/min
0.50
0.006
-0.015
0.015
0.02
Sample deformed at 30 MPa confinement, close to the stress peak
The water was flushed at 4 ml/h
Front speed of 0.253 mm/min
SHEAR STRAIN
VOLUMETRIC STRAIN
WATER FRONT SPEED
Vertical
Vertical
Horizontal
Horizontal
Vertical
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 19
Results: VO04ME
0
-0.035
0.035
0.1
Sample deformed at 40 MPa confinement, in the beginning of the plateau in the stress/strain response
The water was flushed at 3 ml/h
Front speed of 0.19 mm/min
SHEAR STRAIN
VOLUMETRIC STRAIN
Vertical
Vertical
Horizontal
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 20
Results: VO04ME
0
0.25
0
-0.035
0.035
0.1
Sample deformed at 40 MPa confinement, in the beginning of the plateau in the stress/strain response
The water was flushed at 3 ml/h
Front speed of 0.19 mm/min
mm/min
SHEAR STRAIN
VOLUMETRIC STRAIN
WATER FRONT SPEED
Vertical
Vertical
Horizontal
Horizontal
Vertical
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 21
Results: VO05ME
Sample deformed at 40 MPa confinement, close to the stress peak
The water was flushed at flushed at 4 ml/h
Front speed of 0.253 mm/min
0.01
0.2
-0.02
0.02
SHEAR STRAIN
VOLUMETRIC STRAIN
Vertical
Vertical
Horizontal
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 22
Results: VO05ME
Sample deformed at 40 MPa confinement, close to the stress peak
The water was flushed at flushed at 4 ml/h
Front speed of 0.253 mm/min
22
0.1
mm/min
0.49
0.01
0.2
-0.02
0.02
SHEAR STRAIN
VOLUMETRIC STRAIN
WATER FRONT SPEED
Vertical
Vertical
Horizontal
Horizontal
Vertical
Horizontal
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY

## Slide 23
Summary
Objective
Investigation of coupled hydro-mechanical properties with neutrons.
Conclusions
Good control of the water front The 3D water front can be tracked in saturated samples. We are able to get the 3D flow speed map of a hydraulic process. The speed of the front is reduced in the band on a saturated sample.
Future work
Improve the resolution of the tomographies. In-situ hydro-mechanical test in neutrons. Upgrade of the setup for high pressure tests.
CONTEXT | OBJECTIVE | TEST | IMAGE ANALYSIS | RESULTS | SUMMARY