## Slide 1
Ralph Lange, ITER Organization
OPC UA Device Support Overview and Status

## Slide 2: OPC UA Background
Industrial protocol (2006) to interface SCADA to PLCs
  Covers live data, alarms, events, historical data
Based on OPC Classic (Microsoft; 1996), it provides
  Functional equivalence to OPC Classic
  Portability
  Safety (authentication, encryption)
  Information modeling (user defined structures)
OPC UA is gaining traction as universal integration tool
Siemens S7-1500 series PLCs include an embedded OPC UA server

## Slide 3: EPICS Device Support
Based on commercial C++ Client SDK
  Vendor: Unified Automation (~3.5k€ for sources and 1yr support)
  Binaries can be distributed royalty-free
  Platform: Windows and Linux
Prototype by Bernhard Kuner (HZB / BESSY II) https://github.com/bkuner/opcUaUnifiedAutomation
ITER use cases tested by F4E (ITER) and TCS (India):
  S7-1516/1518 embedded OPC UA server
  WinCC-OA embedded OPC UA server

## Slide 4: Status and Roadmap
Requirements Specification v1.0 reviewed and agreed: https://bit.ly/opcua-srs-10
Design done (no formal doc yet)
Implementation is in “usable pre-release” state
  no arrays, no user-defined structures
Feature-complete implementation by end of 2018
Under EPICS license, upstream repository on GitHub: https://github.com/ralphlange/opcua