## Slide 1
pySTXM
Scanning microscope data collection
EPICS Meeting Fall 2018 Russ Berg

## Slide 2
First what is STXM?
Scanning
Transmission
X-ray
Microscopy
X-RAY LENS
Synchrotron
DETECTOR

## Slide 3
What is STXM?
Scanning
Transmission
X-ray
Microscopy
It’s a microscope

## Slide 4
- pySTXM is essentially 2 levels of software, the user level software is written in python using Qt as its application framework and that acts as a client to the STXM devices that are accessed over the second level of software via Epics channel access.
- Target operating system can be Windows, Linux or MAC OS for either level GUI or EPICS, currently all Windows
  pySTXM:
  General software structure
- Rolled my own ca enabled widgets

## Slide 5
Layout that facilitates workflow
“like typed” information organized into panel’s on the screen
Minimal color pallet used to express as few different types of information as possible
Open as few new screens as possible to get at data/parameters
Took Inspiration from:
GUI layout and goals: what I was inspired by

## Slide 6
wanted a structure that would scale as new features and capabilities were realized
GUI layout and goals: what I did want
Type A Stuff:
  Scan definition
  User Preferences
Type B Stuff:
  Scan control
Type D Stuff:
  Device Control
Type C Stuff:
  Data that has been collected
Type E Stuff:
  Log, Info
Type F Stuff:
  Status bar

## Slide 7
What I ended up with: pySTXM UI

## Slide 8
pySTXM UI
Image data
Spectra data
Calibration Camera
Live PMT
Scan control
+ feedback
Status Bar
Data in current data directory
Updates dynamically
Endstation/Beamline Devices
Positioners
Vacuum
Temperatures
Log window
Python console
Status
Scan plugins
Session info
Preferences

## Slide 9
pySTXM
Scan plugin layout -> workflow
Scan plugins ordered from top to bottom in usual order a user needs to work to collect data.
Top -> alignment scans
Down -> image and focus scans

## Slide 10
Visual cues to indicate and impossible scan
pySTXM
Only allow valid scans to be configured/executed

## Slide 11
pySTXM
Easy access to data, Thumbnail viewer
Mouse over brings up tooltip of metadata mined from the hdf5 file(s)
Loads data from disk as it becomes available

## Slide 12
pySTXM
Easy access to data, print or load into a viewer
Right click menu:
“send to Viewer” to load data into separate viewer
“print” data small enough to fit in log book
Right Click

## Slide 13
pySTXM
Easy access to data, quickly load a previous scan
Load previous scan and use to select scan area
Drag and drop data from Thumbnail viewer to central plot to be used to select ROI for a different scan
Drag and Drop

## Slide 14
pySTXM
Easy access to data, Load previous scan for re-execution
Drag and Drop
Drag and drop data from Thumbnail viewer to central plotter
Or
Onto the scan plugins pane to be reloaded

## Slide 15
pySTXM
Interactively build larger view from smaller images
Drag and drop multiple images from thumbnail viewer onto another viewer building up a mosaic of a number of scans
Repeated Drag and Drop
Or select and load multiple files from disk

## Slide 16
pySTXM
Combine coarse and fine images
Repeated Drag and Drop
Images are placed on top of each other based on scan resolution and scan range

## Slide 17
pySTXM
visual tools – Drag the beam
Target shows current position of beam, then use tool to drag it to desired location, ex: I0 optimization

## Slide 18
pySTXM
Calibrate critical stages with little to no expertise
Calibration Camera, roughly calibrate 3 devices in seconds
Frame of video taken from fire wire camera looking inside the UHV STXM tank.
Used to set the initial distance of:
- Zoneplate Z
- OSA Z
- Detector Z

## Slide 19
Cryo-STXM funding partners,
Good image quality at -181 °C
Acknowledgements | pySTXM
Thanks!
Chithra Karunakaran – Science Manager, Environmental & Earth Sciences
Jian Wang – SM Beamline Manager
Jan Geilhufe – SM Beamline Scientist
James Dynes – SM Beamline Scientist
Adam Leontowich- Former SM Beamline Scientist
SM Beamline
Project Mgt.
John Swirsky – Project Manager
CID
Glen Wright– CID Manager
Project funding partners: