## Slide 1: Michael Bree / David Beauregard / Garth Steel Canadian Light Source
BioXAS Data Acquisition Platform
EPICS Collaboration Meeting - Melbourne
November 2018
PyAcq

## Slide 2: Requirements
Acquire / Visualise / Save 1000 x 1000 point scan (~64 Gb)
Extensible to Multiple acquisition techniques:
    Rapid Bidirectional Flyscan / XAS / One Pos. / Two Pos.
GUI responsive at all times – no pauses / stalls
Dynamic visualization (e.g., change ROIs, etc)
Platform independent (Linux, Windows, Mac)
Stand-alone GUI operation (Users can take copy home)

## Slide 3: Rapid Bidirectional Flyscan

## Slide 4: Solution
Client / Server Architecture
Modular Implementation
No EPICS in Client
Restrict EPICS to supporting modules

## Slide 5: System Overview
Client (GUI)
Server
Scan Coordinator
Rapid FlyScan
Beamline Energy
Zebra
SR570
XSP3
Scalar
Mono
Undulator
SSCAN
HARDWARE
Python
High level EPICS
(SNL)
Low level EPICS
Minimal EPICS
No EPICS

## Slide 6
Data
(HDF5)
Scan CFG
(JSON)
TCP/IP
SSCAN
SSCAN
Positioner
Positioner
Positioner
Positioner
Client
No GUI knowledge
No EPICS
GUI
No SCAN logic
No EPICS
Scan
Plugin
Scan
Cfg
Plugin
Scan
GUI
Plugin
Scan
Plot
Plugin
…
…
Scan
Plugin
Scan
Cfg
Plugin
Scan
GUI
Plugin
Scan
Plot
Plugin
…
…
Other
1000 X 1000
64 GB
Standalone Client
Scan
Engine
(Server)
HDF5
Reader
HDF5
Writer
multiprocess
multiprocess

## Slide 9
Thank You!