## Slide 1: Injection Archive System for SuperKEKB
Hiroshi Kaji (KEK)

## Slide 2: Overview
Archive Objects:
EPICS PVs for SuperKEKB accelerator System Configuration:
Standalone PC - OS: CentOS7 linux - CSS archiver - PostgreSQL VME/VxWorks IOC with EVR - CPU: MVME5565 - EVR: VME-EVR-230RF Retreat software:
ROOT
Archiver
Data collector

## Slide 3: Archived data
Followings are recorded in pulse-by-pulse - Shot ID - Injection RF-bucket# - Bunch current before injection (for 1st injection bunch) - Bunch current before injection (for 2nd injection bunch) - Bunch current after injection (for 1st injection bunch) - Bunch current after injection (for 2nd injection bunch) - 1st bunch current at the end of beam transport - 2nd bunch current at the end of beam transport
Followings are record when they are processed - Injection septum angle - RF phase of main ring - etc ...
Using “data collector”

## Slide 4: System Configuration
VME/VxWorks IOC with Event Receiver - Precisely process between every two injection pulse - Collect injection RF-bucket# and shot ID from data buffer
Database server (archiver) - CSS Archiver - postgreSQL
Pulse information is once stored on EVR IOC (data collector).

## Slide 5: Scheme for archiving injection current
Bunch Current Monitor
BCM driven
Bunch Current Monitor (BCM) renews information after every injection. Event IOC collects it!
Event driven
EVR receives which RF-bucket should be checked for next injection via data buffer. Event IOC collects it!

## Slide 6: ROOT as offline software
ROOT website: https://root.cern.ch/ - popular software for data handling (analysis) at High Energy Physics - C++ base - includes PostgreSQL library, GUI, and so on
Offline process with ROOT - retreat data from archiver - put several kinds of data together - draw graphs and histograms

## Slide 7: Data retreat and analysis with ROOT
(Small jitter and 0.2% packet loss caused in CA access)
Injected Current: Iinj = Iafter – Ibefore Two PVs for Ibefore and Iafter are with timestamp. The timestamps should be differ 27ms if they are for one injection process. The matching is performed with ROOT.

## Slide 8: Comparison with Ordinary System
 | Hardware | Measured information | Frequency
Ordinary system | DCCT | All beam current | 1 Hz
New system | Bunch Current Monitor | Bunch current for injection RF-bucket | 25Hz (every injection pulse)
Comments | Bunch current of RF-bucket to be injected is measured in new system. The RF-bucket# is delivered from EVR. | New system can avoid influence of non-injection RF-buckets. | New system records for all injection pulses.
The injected current is evaluated with more sophisticated way than before.

## Slide 9: Performance compared with old system
0.10mA
0.05mA
Beam Current
Ordinary system
New system
The new system has following advantages: - avoid unnecessary influence from non-injection bunches. - distinguish the beam pulse loss.

## Slide 10: Conclusion
We develop the new injection archive system for the SuperKEKB collider.
- It consists of archiver and data collector. - Data collector utilizes the Event Timing System.
Offline data handling with ROOT - retreat data - combine them for each injection - draw pictures
New system has advantages: - avoid the influence of non-injection bunches - distinguish the beam pulse loss