## Slide 1: babyIOC – Control System in a Box from NSLS2
Oksana Ivashkevych and Thomas Caswell, 2018-11-14,
EPICS Collaboration Meeting, ANSTO

## Slide 2: What is babyIOC?
Controls System in Box
64 bit Intel architecture
x4 core 2.56 GHz and 8GB RAM
x3 1Gbit Ethernet interfaces
1x HDMI, 2x miniDP++
3 x USB 3.0
2x UART serial ports
Intel HD Graphics 405
IR interface
Arduino 101-Compatible
diskless SBC
boots and runs from microSD
Building another system like this comes to copying the image to another microSD card.
What is on the image?
Debian Jessie
NSLS2 EPICS distribution built from https://github.com/epicsdeb
compiled areaDetector-3-3-1,
Prosilica IOC example
Bluesky Data Collection Suite
X2Go server.

## Slide 3: “Why babyIOC?
Mobile end-stations, which could travel from beamline to beamline, from one facility to another.
For testing software upgrades in real environment, can be easily put onto a beamline.
To gain confidence in new software at the beamline and accelerator.
To ease learning curve for people new to EPICS
To allow other labs try bluesky Data Acquisition Suit.

## Slide 4: Why Udoo? (not raspberryPi, beagleboard)
Requirements:
    Accomodate several areaDetector IOC (decent CPU muscles and at least 2GB RAM)
    bluesky Data Collection Suite
    Deliver decent performance and customer satisfaction.
We have conducted a research, reviewing many vendors which offer small SBCs:
    Beagleboard
    RaspberryPI
    BoundaryDevices
    Nvidia
    Hardkernel
    PCengineering
    EmbeddedArm
    Udoo
Udoo X86 Ultra from Italian startup was the winner, offering most RAM, CPU power for $356 USD. Project was funded on Kickstarter in 2016.

## Slide 5: Links and credits
https://oksanagit.github.io/babyIOC
Credits
    Oksana IvashkevychBNLvision, driver, babyIOC mother
    Thomas SmithBNL sysadmin, babyIOC father
    Dennis PoshkaBNL babyIOC technician
    Leon FlaksBNLimage conditioning
    Thomas CaswellBNL bluesky deployment
    Matt CowanBNL sysadmin help
    Kevin PetersonANL ideas for disc size expansion
    28ID1, Milinda Abeykoon, Julian AdamsBNL project support
    Christopher StelmachBNL adding cutoff to a drawing.
We are open to community suggestions