## Slide 1: EPICS-FPGA Interface Implementation
Simin Chen
Date: 12 November 2018
Part A

## Slide 2: FPGA Background:
  It is not a “processor”！It does not run a program.
  It is a bulk of reconfigurable digital logic suspended in a sea of programmable inter-connects.
+ Mortar
Bulk of reconfigurable
digital logics
+ Programmable inter-connects
Config binary
Customer expected functionalities

## Slide 3: Local EPICS Interfaces:
  IOC direct memory/register access over PCI Express bus
  Operating system assigns address span for FPGA memory/register
  High-speed DMA read/write available through particular PCIe endpoints
  IOC and FPGA in the same crate (locally)
  Used in µTCA architecture project
Local
EPICS IOC
FPGA
PCI Express
Bus
PCIe
IF
Register 1
Register 2
Register 3
Register 4
Register N
.
.
.
Address bus
Data bus
Memory
block

## Slide 4: Remote EPICS Interfaces:
  Private protocol over Ethernet UDP data packets
  IOC indirect memory/register access over Ethernet connection
  The protocol interpreter bridges the private protocol and the memory/register address span
  No limitation on IOC location
  Use in the FOFB project
Remote
EPICS IOC
FPGA
Ethernet UDP
Eth.
IF
Register 1
Register 2
Register 3
Register 4
Register N
.
.
.
Address bus
Data bus
Memory
block
Protocol
interpreter
Eth.
header
Protocol
header
Protocol
data payload
Ethernet payload

## Slide 5: Remote EPICS Interfaces (Cont’d):