## Slide 1: EPICS-FPGA Interface Implementation
Ross Hogan
Date: 16 November 2018
Part B

## Slide 2: Convergence of FPGA and Processors
Flexibility of a Processor system
Performance of a FPGA
Move the configuration and monitoring out of the data path
Tighter integration for simpler interfacing

## Slide 3: On board Processor:
  FPGA Settings Registers in processor’s address range
  Standard UDP Protocol
  Processor translates Protocol to register read and write.
  No limitation on IOC location
  Use in the ‘FFM’ project
Remote
EPICS IOC
Ethernet UDP
Micro - Controller
Eth.
header
Protocol
header
Protocol
data payload
Ethernet payload
FPGA
Eth.
IF
Register 1
Register 2
Register 3
Register 4
Register N
.
.
.
Address bus
Data bus
Memory
block
Memory
block

## Slide 4: In Chip Processor:
  EPICS IOC running ‘on chip’
  FPGA Settings Registers in processor’s address range
  Device driver reads and writes memory directly.
  Use in the Redpitaya
Channel Access
FPGA
Eth.
IF
Register 1
Register 2
Register 3
Register 4
Register N
.
.
.
Address bus
Data bus
Memory
block
Micro - Processor
EPICS IOC

## Slide 5: Is on board or in chip better?

## Slide 6: Is on board or in chip better?
Yes!

## Slide 7: Is on board or in chip better?
Processor In Chip | Processor On Board
Tighter integration between CPU and FPGA | More flexibility in device choice
Higher transfer speed | CPU can interface to more than one FPGA
Lower power | Varity of protocols